## Slide 1: KS3 d&T contexts short-term shelter
#InspiredbyTheRAF
Notes: Please note; This resource, accompanying resources and associated images, videos and graphics are to be used for educational purposes only and in line with our terms and conditions as stated here. https://www.designtechnology.org.uk/terms-and-conditions-and-policies/

## Slide 2: About this resource
Overview
The Royal Air Force (RAF) is one branch of the British armed forces. Unlike many companies and organisations looking for opportunities, The RAF engineer solutions to real world issues as they arise. One such area that has been tackled before, and the focus of this context is ‘Short-term shelter’.
Area(s) of focus
Structural design, environment, portability, engineering solutions. teamwork.
Links to the National Curriculum
The resource addresses the full design, make and evaluate process, but also suggests investigative and evaluative activities, and relevant focused tasks.
Technical knowledge: CAD, CAM, rapid prototyping, manufacturing processes, maths and science, visual and technical communication.
Included in this resource are a range of images, photographs and videos. Some of the materials in this resource have been created by The Royal Air Force - the D&T Association hereby acknowledges and thanks the RAF for its contribution. Without this, it would not have been possible to produce this, which is freely available to all teachers.

## Slide 3
Suggested level: Late key stage 3*
Duration: Approx. 10-12 weeks
Focus: Innovation, environment, automation
Materials: Multi-materials
Processes: Designing, shaping and forming, manufacturing, science, engineering
Systems: Structural, mechanical, electrical
Responsibilities: Health and safety, environment, sustainability, ethics, six R’s
*you can use the resource at whichever level you feel it is appropriate.

## Slide 4: Contents
Design Context
Empathize
Define
Ideate
Prototype
Test
Focused Tasks
Investigative and Evaluative Activities
Supporting Tasks
Notes: Click the hexagons to go to that section

## Slide 6: Introduction
The RAF are one branch of the armed forces in the UK. They are not a company, nor commercial designers, but they engineer solutions to problems as required, often at very short notice.
The context for this unit is:
Short-term shelter
The following slides will show how the team at The RAF would approach this context in relation to the five main stages of the design process: empathize, define, ideate, prototype, test. You can follow a similar process in your designs and consider how you can design, create and erect short term shelter.

## Slide 7: Emergency response
This context is slightly different from others in the range as The RAF will respond to emergency situations using pre-existing equipment, so we cannot follow the design process they use when creating a new product like commercial companies.
However, we can see how the product was developed for these situations and use emergency responses as just one example of where short-term shelter might be needed.
Hopefully, seeing how this is done effectively for humanitarian aid, will inspire you to create your own designs for multiple applications.

## Slide 8: Emergency response
When The RAF are called upon to provide aid, a process begins that sees
equipment loaded for
fast deployment by air.

## Slide 9: Emergency response
The emergency shelters the RAF deploy are designed to be flat-packed for easy storage and loading. We can see that they can be loaded using simple machinery and human power.

## Slide 10: Short-term shelter
The RAF often deploy temporary shelter in response to emergency situations.
Can you think of other situations where temporary shelter might be required?
If you consider a typical brick or steel building as being permanent, what other temporary shelters, provision or accommodation can you think of?
Are there situations where temporary shelter can be more beneficial than permanent structures?

## Slide 11: Short term shelter
We use the terms ‘short-term’ and temporary to describe shelters that are not ‘permanent’.
This suggests that they need to be erected and dismantled regularly, but what would you class as ‘short term’?
Consider why a traditional brick-built structure is not practical for a ‘short-term’ shelter.
What are the key considerations for a shelter?
How can we ensure a sustainable solution?

## Slide 13: Empathize stage
Your first task is to identify situations where short term shelter might be required. You are looking for a situation that you can design and prototype a solution for. At this stage you are simply trying to understand what some of the problems may be. The more the merrier! There are no wrong ideas/thoughts at this stage! There are many ways that The RAF, and other companies might approach this. Consider trying some of these methods:
‘Estimate process’ | ‘Situation and shelter’ | ‘Needs and values of the user’
Empathy involves understand the wants need and values of others. The RAF have seven questions which they ask to ascertain what is needed in that particular situation. You can see these questions on the next slide, but the RAF refer to this as the ‘estimate process’. | The main concern for the RAF are for the people using the shelter, but yours could be for animals, or for storing equipment. You still need to consider the resource needed, not just to create and erect the shelter, but the resources that need to be stored or accessed from the shelter. | If you are taking a humanitarian approach to this context, try putting yourself in the shoes of the people who may find themselves in need of short-term shelter. How can you ease the burden of the situation they find themselves in? What are their basic human needs, and how can you go beyond these to bring some additional comfort and security to them?

## Slide 14: Seven questions
When dealing with a situation, The RAF ask seven questions which should provide more detailed criteria for the intended action to ensure it meets the needs of the situation.
1. What is the situation and how does it affect me?
This includes environment (where), weather, what has happened, who is there, any supporting units/equipment etc?
2. What have I been told to do and why?
What is the task and why are you being told to do it?
3. What effects do I need to achieve (and what direction must I give to develop the plan)?
Who, what, why, when, where, how?

## Slide 15: Seven questions
4. Where can I best accomplish each action or effect?
Study the area of operation to work this out – i.e. does construction all happen on site or does some need to be done in advance?
5. What resources do I need to accomplish each action or effect?
Work out the required materials.
6. When and where do the actions and effects take place in relation to each other?
The sequence of events e.g. make a plan, assemble equipment, load onto transport, deploy, assemble equipment, occupy shelters.
7. What control measures do I need to impose?
Any restrictions that exists e.g. the location may be an island that can only be reached by sea or air, is there an airfield or does equipment have to be air dropped etc?

## Slide 16: Apply these questions
While we may not be responding to an emergency situation in the same way that the RAF does, we can still use their approach as the basis for how we might tackle the challenge of ‘creating temporary shelter’.
Our needs might have less urgency than the RAF, but this simply gives us more time to develop solutions.
Try adapting these questions to your own chosen scenario or design challenge and see if they help you to formulate a clearer plan for what is required.

## Slide 17: Break down the context
The context is deliberately simple so you can investigate and determine your own approach to exploring design opportunities. This context encourages an empathetic approach to analysing and investigating the design situation which can start with a mind map like this example.
WHERE?
DESIGN PROBLEM
WHY?
WHAT?
WHEN?
HOW?
WHO?
LOCATION
OVERSEAS
HOME
FUNCTION
PURPOSE
MATERIALS
USER
DISPLACEMENT
FESTIVAL
LIGHTWEIGHT

## Slide 18
Notes: Defining the nature of the product

## Slide 19: Define stage
You now need to define your focus. This means you need to state what it is you are trying to do. You need to be precise and clearly state your brief. Who is it for, what will it do, why is it important? To help you with the define stage, try one or more of these approaches:
‘Transporting’ | ‘Environment’
When thinking about the type of shelter you are designing, you also need to consider how it will be transported to the site. For the RAF, this could be on the other side of the world, but even if you are setting up in a nearby field or hall, you would still need to move it to and from locations. Consider this when designing the structure. Will it fold up or collapse? Will it require construction with tools and fittings? Will it all stay in one piece or need to be made up of modular sections? | We may be designing for a particular location at a certain time of year such as a stall for a summer fete, but do you always know what the environment will be used in? How will you adapt to dry or wet conditions, on flat ground or uneven terrain? Can it be erected at night as well as in the day? Many environmental factors can affect how your solutions functions and performs.

## Slide 20: Define stage
Some more aspects to consider when defining your product criteria:
‘Assembly process’ | ‘Strength to weight ’
Unless you are designing a very small shelter, such as for a small pet, the chances are you will need to assemble your shelter on site. As well as how you transport it, how will it be assembled? You cannot assume that everyone will have the technical skills to do this so will you create something simple to assemble or provide clear instructions on how to do it? | For assembly and transport, you will also need to factor in the weight of the shelter. Your product needs to be as lightweight as possible while still providing the maximum strength and support. This is called ‘strength to weight ratio’ and may affect the materials you choose or how they are used in the construction of the shelter.
‘Time frame’
One last aspect to consider is how long the shelter will be used for. You may be using it for just a few hours or a day, but what if its being used for weeks, months or years? Your shelters may function temporarily, but can it perform well over time? Consider how durable and hard wearing your design needs to be based on how long or how often it will be used.

## Slide 21: Technical specification
The RAF do not create products themselves, they would send their requirements to a design and manufacturing company. For this to work, they would need to send very detailed requirements so that the designers can create something that meets their needs.
To do this, they would need to produce a ‘Technical specification document’.
For the situations the RAF work in, the specification would contain details about purpose, capacity, materials (if necessary), strength (to survive environmental conditions) and may also mention heating, duration, time and manpower requirements for erection, size when packed and how it can be transported.
What would a technical specification for your intended purpose need to include so that you could be sure to meet the needs of the user or the situation?

## Slide 22: Define stage
Consider these aspects when defining and designing your product.
Function
Purpose
User
Authenticity
Innovation
What it is intended to do?
Who it is intended for?
How it works
Is it relevant, realistic and feasible?
What unique features it has

## Slide 23: Define stage
The context ‘Short-term shelter’ provides an overview of the design opportunity, but it may be useful to encourage students to create their own more focused design briefs, so they have some criteria to refer back to when investigating the context and developing their own solutions. It could be as simple as:
“Design a flat-pack tool-free shelter for use at a festival”
A simple statement of the design problem to be solved 

## Slide 25: Ideate stage
As the product is designed by an external company, it is not possible to show the process from The RAF’s perspective, but the process followed will be similar to the one you have used in school.
Following the creation of a brief or technical specification, initial ideas will be created which can be shared with the client. These only need to be rough ideas at this point, but the best of these can be considered for further development.
Using a variety of methods such as drawing, CAD, models, mock-ups, renders etc. the wide range of design ideas converge towards a final solution. This might involve adding new features or removing elements that don’t work.
Eventually a design will be produced that is ready to be realised in physical form either as a scale model or a full-size prototype which could be a combination of real components and mocked-up elements.

## Slide 26: Ideate stage
The double diamond model shows how ideas and thoughts diverge (open up) at certain stages in the design process such as the empathy stage when considering the needs of others and investigating the problem. All the ideas then need to converge (narrow down) so that the focus can lead to a solution.

## Slide 27: Ideate stage
You now have a brief, so it is time to consider lots of different ideas for your outcome, so you have lots of design choices. It is also a chance to eliminate as many potential problems as possible. These don’t need to be detailed and accurate at this stage. Try some of these ideas:
‘Function over form’ | ‘Share ideas’ | ‘Get inspiration’
The RAF don’t actually design products, but even those that they are involved with are considered utility items and they are more concerned with how they function than how they look. Think about the product you use everyday. Is it more important how they look or how they work? What about your shelter, will it be more functional than aesthetic? | Even though the RAF don’t design their own products, they work with the designers who are used to sharing their ideas with clients. These ideas could be in the form of sketches, CAD models or scale models. These could be static to show how the structure looks, or dynamic with moving parts to show how it will function for assembly and disassembly. | We all need inspiration for our ideas, so keep looking at other products to see if they can help with your design. Often, these ideas can come from unexpected sources. You might even get ideas from looking at unexpected sources such as nature. For example, tents used to look more like houses, but now they use a shell-like structure more like that of a snail shell.

## Slide 28: Sketch ideas
The quickest way to generate ideas is to sketch your first solutions….

## Slide 29: Collapsible structures
For the shelter to be temporary, it would need to be stored before, and possibly after, use. For the structure to be erected quickly, it might incorporate some collapsible mechanisms.

## Slide 30: Fixed structures
Your shelter will need to be portable, but it can still be constructed into a rigid structure rather than being a flexible or folding structure. What makes it rigid is the reinforcement which, when using solid beams or panels, is inherent in the material. A fixed structure is usually not designed to be collapsed and transported, but you may still learn a lot about strength and rigidity from studying them as well as appreciating how they differ from temporary structures.

## Slide 31: CAD structures
CAD can be a useful tool for designing structures and we can also use features such as FEA to see how they will perform under load, or even simulate earthquake conditions.

## Slide 32: Short-term shelter
Here are just a few examples of shelters that are also intended to be used short-term.

## Slide 33: CAD mechanical designs
We can also use CAD to quickly duplicate components for a structure and even test these out mechanically

## Slide 35: Prototype stage
At some point you will need to prototype your idea(s). This is to see if what you are trying to do, will work or not. Early prototypes may be made of modelling materials such as card or foam making it easy to work with using basic tools and equipment. You might then move on to more ‘resistant’ or hard materials to test out the prototype in terms of function and performance.
‘Feedback, then refine’ | ‘Scale models’
It is important to get the mechanical or structural aspects of your shelter made so they can be tested. This may be in the planned environment or could be done in the classroom or on the school fields. Prototypes are important so you can share your designs with the client who can also see what needs improving or refining. Consider the purpose of the prototypes you make. Are they for testing a mechanical or structural concept, or for humans to interact with and test for space, ergonomics etc? This will influence the type of prototype you make. | This is likely to be a large-scale project so it will be difficult to make a full-sized outcome to test. What elements do you need to demonstrate that this will work and could that be done with scale models? These could be made from card, balsa, lollipop sticks or even art straws. The point is to see how your design functions. Consider making a detailed scale model in CAD and producing parts using 3D printing and laser cutting. Does your design have fixtures or moving elements that you can make in a smaller form to test that they work?

## Slide 36: Prototype stage
This context lends itself well to both physical and CAD modelling as a means of developing an outcome to help clean up the environment.
You could use rapid prototyping methods such as 3D printing in the development and prototyping stages so quick results can be achieved. You could also use software to test the structural stability of a solutions as well as calculating its weight and checking any mechanical functionality.
The final prototype could be created with greater accuracy by making use of CNC machinery. The RAF engineer many products in metal so you may want to take a more technical approach and prototype using a lathe, mill or other machine if working in metal.
For making skills that this resource could address, refer to the Curriculum Units relevant to the materials or processes you wish to cover in your teaching.

## Slide 38: Test stage
‘Test against original aims’ | ‘Visual’ | ‘Measurement’
The RAF would never deploy products that were not tested, as human lives might depend on the product working effectively. While testing, return to your original aims. Getting feedback from those who will use your product is vital. | There are four main ways to test a product: Visual tests consider the aesthetics or look of the product. For the RAF this is a secondary concern, but your product might be to promote or sell items so it could be more important how it looks. | This can be related to size, weight, cost, portability etc. For the RAF, the cost will be less important than the lives it saves or improves. For a shelter that needs to be transported, weight will be a prime concern and, when in use, the size for people and storing objects will also be very important.
The iterative design process requires the outcomes to be tested against the original intentions so you can see how well your design would meet the needs of the user. This could involve testing the outcome yourself or giving the prototype to others to use and evaluate. Consider these approaches:

## Slide 39: Test stage
It is important to refer back to the [name of specification here] so we can evaluate how well we have met the original brief.
‘Function’ | ‘Performance’ | ‘Overall effectiveness’
How a product functions is a key aspect of the design. Does the structure fold as intended, do doors or shutters open and close properly? Can all connections be accessed and do they work? The look of this product is likely to be less important than its ability to function as intended. | This is related to the function, but considers how a product is used over time. It may be assembled once, but can it be rebuilt repeatedly? If it were air-dropped, would it still perform as expected time after time? If not, consider how it could be redesigned to improve its performance. | With all these different factors considered, how would you rate the overall effectiveness of your prototype? The RAF are always monitoring the effectiveness of the product and systems they use, and for a designer, this is part of the iterative design process: constantly monitoring and improving solutions to make even better products!

## Slide 40: Focused Tasks
Whilst the brief in this context is regarding short-term shelter, there are a number of focused tasks you could use in this unit of work to support the design process or simply use the context as a vehicle to deliver these particular skills. The following are just some it lends itself well to:
‘Structural models’ | ‘Amenities’ | ‘Collapsibles’
Make a scale model of your shelter design using basic modelling materials such as card and paper. Avoid using block materials such as foam as this would not represent thin lightweight structures. Consider using lollipop sticks for levers/linkages and stretching thin fabrics such as Spandex to represent materials for your shelter. Try and use materials that will represent the real-world materials used, but in a scale form. | A structure is just one aspect of this project. Shelters will need amenities such as electricity, water, air conditioning, heating to name a few… Make a list of the amenities, resources, supplies etc. that your shelter would need. Prioritise these in terms of importance and draw a plan of the shelter to show where key features might be placed. | You are designing a temporary shelter so this will likely involve collapsing/portable structures incorporating mechanisms. Explore a range of mechanisms that could be used to collapse a structure. Could they be designed so that they simply ‘pop up’ or will your design require elements that need to be assembled on site?

## Slide 41: Investigative & Evaluative Activities
The investigate, or research, element of this project could encourage more detailed exploration of the products on the market, possibly available to buy or in the local area (think pop-up stalls / marquees). There are numerous opportunities available to investigate and evaluate materials and products in this context.
‘Types of shelter’ | ‘Natural disasters’ | ‘Environmental challenges’
What is a shelter, and what defines its purpose? Investigate different types of shelters for a range of applications. Produce a chart to show any key features that certain types of shelter might share. Are there any common aspects in terms of construction or application that you can use to inspire your own designs? | People are often displaced from their homes due to natural disasters such as earthquakes, landslides, floods etc. Investigate the immediate needs of people who have suddenly found themselves without homes or shelter. Look through the news from the last decade and see what natural disaster have occurred, the causes (if any) and the effects these had on communities affected. | We often make projects in our school workshops, but what about taking these products into the world outside. What obstacles might we have to overcome when delivering these shelters to their intended locations? Investigate a range of different and challenging environments and list the difficulties you might overcome. For example, compare a jungle location to one with ice and snow.

## Slide 42: Empathize tasks
‘Estimate process’ | ‘Situation and shelter’ | ‘Needs and values of the user’
Use, or adapt, the seven questions that the RAF use, to suit the situation: What is the situation and how does it affect me? What have I been told to do and why? What effects do I need to achieve and what direction must I give to develop the plan? Where can I best accomplish each action or effect? What resources do I need? When and where do the actions and effects take place in relation to each other? What control measures do I need to impose? It may be worth choosing a situation beforehand. Possibly information from here may be a starting point to see natural disasters in recent years. Students can then research the incident to help them with the 7 questions. | The main concern for the RAF is providing shelter for human beings, but the shelter might be for humans, animals or even to store products. In order to meet the needs of the user or the intentions of the shelter consider these factors: Purpose of the shelter – why do we need a shelter in the first place, what are we sheltering from? Storage – what will actually need to fit into the shelter? Where is the shelter needed? – factors such as the environment, location, weather, and climate will affect how the shelter will be transported, erected and used. How portable does it need to be? – is it intended to be carried by one person, or a team? What additional vehicles or equipment might be needed to move it around? Access and amenities – does the shelter need supplies of water, electricity, gas? Does it need internet access? | Try to get students to place themselves into the shoes of the people working with or using the shelter. This could be those working with it as well as the end user. Remember that someone has to get the shelter to site. Consider its journey from storage to site. Who needs to interact with it, set it up, connect services and supplies etc? This will very much depend on the purpose of the shelter, but it will inevitably require human interaction. With the end users’ expectations established, how can you meet and potentially exceed those expectations? Consider also the needs and values of the end user. If someone will be ‘living’ in the shelter, how can we meet their needs and values such as: Food preparation and washing Eating Sleeping Getting dressed Bathroom Prayer or isolation You may get students to consider such USP’s (unique selling points) for the product, assuming it is pitched as a commercial solution, unlike those used by the RAF.
Notes: Feel free to edit / use these with your class as appropriate. Change the wording and share with students if you wish, or use to help your own planning.

## Slide 43
Notes: You may wish to show students a possible approach to this context. Could they design a scale-version of something like this? You may want to withhold this video until after they have created theirs to avoid design-fixation.

## Slide 44: Define tasks
‘Transporting’ | ‘Environment’
Temporary shelter will need to be stored when not in use and also loaded onto vehicles for delivery. To help with this you may want to investigate different tents, from child’s pop-up play tents, to expensive outdoor tents to see how they are constructed and fixed. Similarly you (or students) may wish to give a size constraint e.g. a temporary safe-space bed for an autistic child may need to fit into a hand-luggage space on an aeroplane. Consider a technical specification: A few questions to ask before defining the technical specifications: How can it be compacted down to take up the least space when stored? Will it fit into a bag (or bags) to be easily carried? Would it fit into a standard car boot, or would it need a van or truck? Is it robust enough to be thrown/airdropped Will I need any specialist tools to erect the shelter? Is any specialist skill or knowledge required to erect the shelter on site? Will it need any specialist connections (power, water etc.)? Can it easily be repaired or can parts be replaced? How many times is it expected to be used before it will it need to be replaced? | Understanding what the local environment is like, is key, especially if used overseas. However, even understanding what the area is like for a pop-up craft stall is important. Is it hard ground or can we add pegs to the ground? Is it windy and things will blow away easily? Is there power, or will I need a generator? Do I need to fit it in a lift or carry up stairs?... A research task based on the local area is a worth-while activity, possibly even using Google maps if the area is overseas. Find out what the weather is like, what local materials are available, what is access like?
Notes: Feel free to edit / use these with your class as appropriate. Change the wording and share with students if you wish, or use to help your own planning.

## Slide 45: Define tasks
‘Assembly’ | ‘Strength to weight’ | ‘Time frame’
The size of the shelter means it’s likely to be erected on-site. No matter who the user is, ideally it needs to be simple. Consider looking at something like Lego instructions, or for IKEA furniture. What have they done to mean that things are as simple as possible? This may be diagrams, but also parts in numbered bags, coloured components etc. Getting students to carry out these activities can prove useful. Even looking under the bonnet of a car can be useful – how have the designers made a potentially overwhelming, stressful task, easier for the user? | This may lend itself well to a classic, fun task of constructing a structure that holds an object but is as light as possible. Consider using dried spaghetti or sheets of newspaper to hold an object aloft. The winner is the one that uses the least material. The likelihood is, that the shape / construction is the key – think triangles. This is also a good example to explore modern, composite materials such as carbon fibre, graphene and more and how they are used in defence, sports and more. | How long will the shelter be required for? While the RAF are aiming to support / save lives, we should all be considerate of making things that are durable and/or can be repaired easily. Considering the 6 R’s: Recycle Rethink Reduce Reuse Repair Refuse Which of these could/should be utilised in the shelter design, and how?
Notes: Feel free to edit / use these with your class as appropriate. Change the wording and share with students if you wish, or use to help your own planning.

## Slide 46: Ideate tasks
‘Function over form’ | ‘Share ideas’ | ‘Get inspiration’
The RAF work with utility equipment, products that serve a particular purpose. They are not advertised or sold so it’s less important to them how they look. As such, testing of the ideas and prototypes as you go through is vital, more so in this context. Trying elements and testing them is key. You may wish to create an outdoor or table-top shelter to protect from the rain as a group exercise. The Scouts, in collaboration with Save the Children have some good resources and ideas here. | Because the RAF don’t create their own products, they rely on the designers or engineers sharing their ideas as the design progresses. When working in groups, sometimes it can be hard to think of a range of ideas. Consider designing/developing in isolation before coming together as a pair or group. This way students get the change to formulate their own ideas without the noise and pressure of others sharing their ideas. The context may also lend itself better to designing directly with materials and making (as opposed to drawing ideas, as some children will find it hard to draw and know if they will work.) | Consider having a handling collection in the class of things that may help inspire students when designing and developing. Obvious ones include tents and play-tents. It may be that many have the need to do waterproof shelters of some sort, so get students to consider other ‘things’ that are waterproof –it may be shapes of man-made structures, finishes, textures, nature etc. The following may help to gather items and help secondary research.. Analogous solutions - this is when a product for a completely different application inspires an idea for your design. Think about what a syringe is used for, but they are also used to make pneumatic toy grabbers Biomimicry – this is where nature inspires design. Tents used to be inspired by, and shaped like, small houses. Someone saw how a snail’s home (its shell) was formed and now most tents use a similar type of structure. Lateral thinking – sometimes you need to take a completely different view of the problem and move away from existing ideas of ‘how this has been done’. This is how innovative new products are created. Consider a game where you set ‘rules’ such as ‘it cannot look like a tent’, or giving them materials that are not waterproof – how can they overcome this? – can they apply a finish, can it be shaped to make it suitable?
Notes: Feel free to edit / use these with your class as appropriate. Change the wording and share with students if you wish, or use to help your own planning.

## Slide 47
Somewhere in this context it feels we need some FT’s/Something about taking a sheet and making it hold the most material, or protect the most. Roll, zig-zag, cut to create a canopy/shade etc. Must be some paper-engineering things we can borrow from?

## Slide 48: Form and function
These products combine functionality with an attractive form and are considered icons of design. Would you agree with them all?
Notes: Feel free to edit / use these with your class as appropriate. Change the wording and share with students if you wish, or use to help your own planning.

## Slide 49: Prototype tasks
‘Feedback, then refine’ | ‘Scale models’
A prototype is not actually a product, it is a first version of what may become products. The purpose of a prototype is to test out concepts in a physical form so that you can make improvements. It is also important to be able to share a physical outcome with your client so that they can see what it looks like and how it functions. Putting a product into full scale production can be a very expensive process, and even more expensive if you need to redesign it due to design faults. You will need to see and evaluate the form of something. Could this be done quicker using 3D CAD, and a solution created more easily than making a real model? With access to 3D printing and laser cutting, small scale physical models can also be created. Are you testing mechanical or structural principles? Again, 3D CAD software can often be used for this purpose if it will save time. Remember that you can still 3D print your parts from those 3D models. Don’t get hung up on a prototype replacing a ‘finished product’ in the design process. Any working model, mock up or even detailed CAD model or assembly that allows you to test certain principles and feedback into the iterative design process is a useful prototype. Explore a range of virtual and physical outcomes, use AI to generate more effective structures, and explore your designs through AR and VR where you can virtually walk through larger structures. | If you are designing a shelter large enough to accommodate humans, it is likely to be quite a large outcome. This will be difficult, possibly impossible, to realise full size in school. For this reason, architects and engineers often make scale models Making a scale model means you can share your design with your client or potential customers as the product develops. If your prototype is for mechanical testing, you can get instant feedback on how strong it is or how well it performs, even when it’s made to scale. A visual model may be more concerned with aesthetics; how it looks, feels, sounds. You can show this to stakeholders to get their thoughts on how it looks. You can combine your scale model with full size components or create a test rig such as a frame element to test the weight it can take or how it folds up. Often these one-off components can be tested to extremes/destruction. Consider combining a range of prototype elements to use with a scale model but, whatever option you take, record the process and the feedback from testing and evaluation, as well as feedback from stakeholders and review the comments with a view to making these improvements to your designs.
Notes: Feel free to edit / use these with your class as appropriate. Change the wording and share with students if you wish, or use to help your own planning.

## Slide 50: Test tasks
‘Test against original aims’ | ‘Types of test’
Testing with users is an important aspect of User Centred Design. They should be involved throughout the process, but this is your chance to get valuable feedback on what may be the final proposal. Where possible the shelters should be tested as intended. This is likely to be a scale model in some instances, and so some judgement will be needed as to whether the ‘real’ solution would act in the same way or not. Get students to make predictions beforehand and see if they match what was predicted after testing. Following an approach that is familiar in science lessons may be useful here. Trying to simulate real world conditions can be hard. Rain doesn’t only fall vertically, the ground isn’t always flat, your hands aren’t always clean, free of dirt and grease and warm. Get students to refer back to their environment analysis and explain how they should test to simulate these environments. Students should then offer improvements and modifications for further iterations. Students should also refer back to their original brief or technical specification and discuss how well the prototype meets these criteria. | Your prototype needs testing, so you need to identify the most suitable and reliable methods for testing. These might include: Visual/aesthetic tests. What the outcomes looks like. This can be very subjective as people will have different visual tastes. Should it blend-in or stand out? Measuring tests. These are more objective as you can test and evaluate the size or weight of the design and that if fits within the parameters you define. This is particularly relevant to this context. Functional tests. Does the object function as intended? Performance tests. This is different to function and considers how it works over time, under stress etc. This may require additional time to test and get the results. Consider also: Virtual vs Physical. Do you get the same results with both virtual CAD tests and real-life? Destructive testing. How much force does the product withstand before deforming/breaking? Does this exceed expectations and minimal amounts? (Be sure to carry out a detailed risk assessment for any destructive testing that may have the potential to cause injury)
Notes: Feel free to edit / use these with your class as appropriate. Change the wording and share with students if you wish, or use to help your own planning.

## Slide 51: Level of challenge
Design contexts increase in challenge for each of the KS3 years. By reducing the scaffolding and support you can develop opportunities for more individual and innovative work to be produced.
Closed
Task
Open
Task
Context with Brief
Supported Context
Open Context
Create a temporary shelter that can be realised in CAD or physical model form.
Create a working prototype of a temporary shelter which may be scaled down or full size to test out the concept.
A fully working solution to the context that can be seen in model form, possibly animated in CAD, and realised as a working prototype ready for testing and evaluation.
Increasing level of challenge