## Slide 1: KS3 d&T contexts Carrying cargo
#InspiredbyPure
Notes: Please note; This resource, accompanying resources and associated images, videos and graphics are to be used for educational purposes only and in line with our terms and conditions as stated here. https://www.designtechnology.org.uk/terms-and-conditions-and-policies/

## Slide 2: About this resource
Overview
Pure Electric are manufacturers of electric scooters. This context asks you to consider ‘carrying cargo’ on bikes, scooters or other relevant methods of transport.
Area(s) of focus
Transport, luggage, safety, ergonomics, manufacturing.
Links to the National Curriculum
The resource covers a full design, make and evaluate process, but also suggests investigative and evaluative activities, and relevant focused tasks as well as how products are manufactured in industry.
Technical knowledge: CAD, CAM, modelling, ergonomics, rapid prototyping, manufacturing processes, maths and science, visual and technical communication.
Included in this resource are a range of images, photographs and videos. Some of the materials in this resource have been created by Pure Electric - the D&T Association hereby acknowledges and thanks Pure Electric for its contribution. Without this, it would not have been possible to produce this, which is freely available to all teachers.
Notes: General information about the resource to help you decide if it is right for your needs.

## Slide 3
Suggested level: Mid/late key stage 3*
Duration: Approx. 10-12 weeks
Focus: Transport, UCD, ergonomics, anthropometrics, sustainability, innovation
Materials: Multi-materials, but with a focus on textiles
Processes: Designing, shaping and forming, manufacturing, science, engineering
Systems: Mechanical, structural, CAD, CAM
Responsibilities: Health and safety, sustainability, ethics, six R’s
*you can use the resource at whichever level you feel it is appropriate.
Notes: A summary of the resource so you can check it meets your curriculum requirements

## Slide 4: Contents
Introduction
Empathize stage
Define stage
Ideate stage
Prototype stage
Test stage
Implement stage
Focused Tasks
Investigative and Evaluative Activities
Supporting units

## Slide 5
Notes: Introductory video

## Slide 6: Introduction
Pure Electric are manufacturers of electric scooters (e-scooters) based in Glastonbury.
The context for this unit is:
‘Carrying cargo’
The following slides show how the design team at Pure Electric would approach this context in relation to the five main stage of the design process: empathize, define, ideate, prototype, and test. They also look at the implement stage which is where the product would be put into production. You can follow a similar process to create your own solution to carrying cargo on bikes and scooters!
Notes: Introduction to the context

## Slide 7
Notes: Empathize video

## Slide 8: Empathize stage
Your first task is to put yourself into the shoes of the potential user you are designing for. At this stage you are simply trying to understand what some of the problems may be. The more the merrier! There are no wrong ideas/thoughts at this stage! There are many ways that Pure Electric, and other companies do this. Consider trying some of these methods:
‘Competitor analysis’ | ‘Online consumer research’ | ‘In-person consumer research’
In business, it is important to know what is already on the market. These are companies competing for your business. Looking at the market is a passive way of understanding what is happening on the market and where you can build on good ideas or see a gap in the market. You could rate or grade existing solutions and use this data to help define your own criteria. | The user is the customer and Pure Electric use online platforms to engage with their users. You may be able to do an online survey or questionnaire. Be sure to frame your questions in an unbiased way as this data will lead the direction of the product. If the majority of those interviewed say they would carry groceries on their scooters, this may well be a focus of your product. | Research is not just done online. It’s important to observe and talk to the users in person. We need to meet their individual needs so we cannot assume to know what those needs are. Consider those in your target market who you may already know and aim your research at them to better understand their needs. This may be people carrying shopping, not just those riding an e-scooter.
Notes: Click the headings to get further information. Feel free to delete / edit the table to provide more or less for your students.

## Slide 9: Empathize stage
To design for others, Pure Electric consider the user from concept to product launch and beyond. User Centred Design (UCD) is an approach that considers the user in all aspects of the design process as well as their needs, wants and values.
Your initial research should define the users for your product as the designers at Pure Electric have done. The user might also represent the product’s intended ‘target market’.

## Slide 10: Break down the context
The context is deliberately simple so you can investigate and determine your own approach to exploring design opportunities. This contexts encourage an empathetic approach to analysing and investigating the design situation.
WHERE?
DESIGN PROBLEM
WHY?
WHAT?
WHEN?
HOW?
WHO?
LOCATION
HOME
PARK
FUNCTION
PURPOSE
MATERIALS
USER
NEEDS
DAYTIME
NIGHT
CARGO
Notes: A mind map approach to breaking down the context. Edit to suit.

## Slide 11
Notes: Defining the nature of the product

## Slide 12: Define stage
You now need to define what we want to achieve. This means you need to state what it is you are trying to do. You need to be precise and clearly state your brief. Who is it for, what will it do, why is it important? To help you with the define stage, use one or more of these:
‘Viability’ | ‘Planning ahead’ | ‘Statement’
We know that carrying cargo is a problem, so we need to make sure that any solution is viable; that it will solve the problem and appeal to customers. Pure Electric sign a business agreement milestone. This is used to give an indication as to whether it’s a good idea to progress! Are you able to do the same on some of your selected ideas? | As well as the potential market, designers need to anticipate how long they will need to spend on designing and prototyping the product as this affects the final costs. One way is to create a Gantt chart where you set the start and end dates and how long you would spend on the main areas of ideate, prototype and test anticipating at least two or three loops of this process. | It may help to put in a statement what the product should do. This is like a specification, but it can be more of a statement of intent where you state what unique elements it will have, what is unique selling point will be, how it will stand out from the competition etc. Think ahead of what the sales advert may have on it! You can grade or score your ideas against these criteria when developing your solution.
Notes: Click the headings to get further information. Feel free to delete / edit the table to provide more or less for your students.

## Slide 13: Define stage
What do we mean by ‘carrying cargo’?
Cargo was originally the term for good transported by boat, but it has developed to cover goods typically transported in bags, boxes, crates, drums, or barrels.
For the purposes of transporting items on a scooter or bike, this could mean:
carrying a bag such as a rucksack or handbag.
transporting items such as groceries or tools.
While you can’t transport another person, you may have a small pet that you wish to carry as ‘cargo’.
Safely storing your personal possessions while in transit.
Can you think of any other applications for ‘carrying cargo’?
Notes: This may be a good task to do as a class, either using post-it notes or consider an online platform such as Google Slides, or Miro.

## Slide 14: Define stage
Consider these aspects when defining and designing your product.
Function
Purpose
User
Authenticity
Innovation
What it is intended to do
Who it’s intended for
How it works
Is it relevant, realistic and feasible?
What unique features it has
Notes: Five key criteria to consider when designing

## Slide 15: Define stage
The context ‘carrying cargo’ provides an overview of the design opportunity, but it may be useful to encourage students to create their own more focused design briefs, so they have some criteria to refer back to when investigating the context and developing their own solutions. It could be as simple as:
“Design a backpack that can attach to a scooter when travelling”
A simple statement of the design problem to be solved 
Notes: Suggesting a brief for the context

## Slide 16: Specification
A Product Design Specification (PDS) provides more detailed criteria for the intended outcomes to ensure it meets the needs of the customer or the market.
While the design brief is a starting point, the PDS can be very specific in terms of size, materials, production, packaging, cost etc. The production of a detailed PDS is a requirement at GCSE so it is a good idea to incorporate them into your KS3 design work.
A common list of criteria might include: aesthetics, cost, dimensions, function, human factors, social, moral and environmental concerns, manufacture, materials, safety, target market etc.
Notes: Do students need to write a specification for this context?

## Slide 17
Notes: The ideation stage explained by a member of the design team

## Slide 18: Ideate stage
You are trying to consider lots of different ideas for your solution to this context, so you have lots of design choices. It is also a chance to eliminate as many potential problems as possible.
These don’t need to be detailed and accurate at this stage. Try some of these approaches:
‘Looks like/works like’ | ‘Competitor and mood boards’
We can often approach concept generation by focusing on what a product will look like. This is the ‘image’ customers see in a brochure or on a website however, there is no guarantee that these concepts will actually work or be viable solutions. The works like is how we ‘mock up’ working concepts even if they don’t look like a finished product, they can look rough – but prove it will work. These two approaches will often run in parallel as the design develops. | Mood boards are a way of looking at brands, colours, materials, style and form etc. so these can be used to inspire new ideas for your product. Competitor boards take this a step further by allowing us to see similar or complimentary products that are already on the market. These are not intended to be copied, but it is important that your product is in line with current trends and expectations even if you plan to offer something new and exciting.
‘Try them out’ | ‘Ideate vs prototype’
It is important to not just look at existing products, but to try then out where possible. If you cannot access new products, you could try adapting existing cargo solutions to use with your bike and scooter. This will help you see where the problems may be and help develop your designs. | Pure Electric ideate and prototype all the time. It’s important to test ideas as you go along to make sure they are realistic and likely to work. Make sure you show/explain how you tested it. Ideas don’t always need to be drawn; consider using foam, wire, card and more.
Notes: Click the headings to get further information. Feel free to delete / edit the table to provide more or less for your students.

## Slide 19: Ideate stage
Ideation is the process of realising our ideas then developing them towards a prototype. Try some of these in this context:
Quick sketches: spend 5-10 minutes per sketch to avoid design fixation.
CAD ‘sketch models’: use a simple CAD package to generate quick and simple ideas.
Use materials – for example, wire, foam and card to create solutions.
With all of these methods it’s time to throw caution to the wind and just get some quick ideas down. It may also help to have a scooter (or bicycle) in the class to use / look at. Where could the carrier attach to? Can I model around the product?
Getting stuck for ideas?
Try the SCAMPER or SCARED approaches to generating new ideas.
Think differently, Could we use an unusual material? How could it attach? How can I open it?...
Notes: Some suggestions of how to ideate and develop ideas

## Slide 20: Ideate stage
Different approaches to the design can be taken, but setting limits or restrictions can actually help to drive creative solutions.
Can you redesign an existing solution?
What ideas can you create that are made from a single part or shell?
Could your design be modular, so the customer only buys the parts they need?
Could you make it multifunctional so that additional pieces are needed to provide more than one purpose?
Can you reduce materials in your designs?
Can you design something that can be easily repaired or recycled?
Can you standardise the components or reduce the need for tools and fittings?
Notes: Some considerations for how to generate ideas for the design

## Slide 21
Notes: Prototype video

## Slide 22: Prototype stage
At some point you will need to prototype your idea. This is to see if what you are trying to do, will work or not. Your prototype may incorporate some sort of mechanical fastening. How will people operate it? Will it be worn or fixed to the scooter or bike? What do you need to prototype to test it out?
‘Cut and shut’ | ‘Increased resolution’ | ‘Aspirational model vs functional model’
It can be difficult to create a prototype from scratch, especially in the earlier stages of design. Consider taking elements from existing objects such as racks, straps, catches etc. and glueing them together to quickly create your ideas for testing and improvements. | If the first prototypes are ‘rough and ready’ they will increase in quality as they develop. Pure Electric refer to this as ‘increasing the resolution’ and this might mean simple card models develop into more complex prototypes using manufactured components. | Similar to the ‘looks like/works like’ concept from the ideate stage, you can make an aspirational model that looks like the intended finished product. This might be a CAD model or using AI to generate various solutions from a simple model that you could show to your client or target market. Your functional prototype will work so you can test out the functionality.
Notes: Click the headings to get further information. Feel free to delete / edit the table to provide more or less for your students.

## Slide 23: Prototype stage
This context lends itself well to both physical and CAD modelling as a means of developing a working prototype.
Polymorph, plasticine, and foam are all great materials for realising organic or curved forms effectively. Card and paper can be used for more box-like shapes. Textiles will naturally be a solution where flexibility is needed or if something is worn and paper templates could be made first. Scale vacuum-formed shells can be used for hard-cased products.
You could also use laser cutting or 3D printing in the development and prototyping stages so quick results can be achieved.
For making skills that this resource could address, refer to the curriculum units relevant to the materials or processes you wish to cover in your teaching.
Notes: This context can make use of CAD and physical modelling

## Slide 24
Notes: Test stage video

## Slide 25: Test stage
‘CAD tests’ | ‘Real material tests’
It can be very expensive (and time-consuming) to make a product and test it, only to discover it breaks/fails and you have to start again. Recent developments in CAD mean you can now do some virtual testing to see how materials will react to various conditions. For example, using simulation such as FEA you can see how a product or component will perform under load before you make a prototype. Many CAD programs offer this feature, and it is a useful process to save time and money when designing a product. Try using different materials in your product and see how they react to the simulations. | However, it is also important to test the prototype with real materials before manufacturing, but this can be time consuming and expensive, as well as requiring specialist testing equipment. You can do tests on existing components to see how materials respond as well as making simple test rigs that focus on functionality rather than aesthetics. Try doing static load testing by putting increasing weights into your cargo carrier. Fatigue tests will show how the same prototype performs in constant use.
The iterative design process will require the outcomes to be tested against the original intentions so you can see how well your design would meet the needs of the user. This could involve testing the outcome yourself or giving the prototype to others to use and evaluate. The following are methods discussed in the video:
Notes: Click the headings to get further information. Feel free to delete / edit the table to provide more or less for your students.

## Slide 27: Implement stage
In school, a design project is often finished when you make, test and evaluate the finished prototype but this is not the same process used in industry.
Pure Electric, like many companies, consider the manufacture and distribution of a product as part of the design process from the very beginning.
This will involve additional processes such as developing the prototype further for production, making a pre-production version for live testing, registering and protecting the design, tooling, costing, developing packaging and promotional material, tracking costs, and how it will be advertised and marketed.
All of this will need to be done before a product even leaves the factory and most of it is done before it is even manufactured!

## Slide 28: Implement stage
‘Target cost’ | ‘Bill of materials’ | ‘Price points’
Product price points are key buying decisions for users. You need to define a suitable price point for the product which would also be in the original specification. If it’s a higher priced item, it needs to look like a premium product. If low cost, then it can be more of a ‘budget’ looking option but should still be functional and attractive. | A bill of materials is used to track the cost of each part and therefore the cost of the overall product. In the early stages of development, this is something you could estimate using existing materials and components but near in mind that changing costs of components will mean the cost of the finished product will go up. | Estimating costs may mean that certain ideas have to be abandoned. For example, a hard-shell carrier might cost £80 to make compared to £10 for a soft fabric option. The selling cost is around three times the production cost so that would be £240 vs £30. Other costs include packaging, shipping, advertising, marketing and much more. Consider just how much profit you could make from your product and factor this in while designing it.
Your design work will usually end after you have tested the prototypes outcome, but what happens next when the product goes into production? How do prototypes become commercial products or systems? What process would need to change to be able to create your design on a larger scale?
Would this affect your choice of materials, fittings, components of finish?
Would your design need to be changed so it could be produced on a larger scale. Consider these:
Notes: Click the headings to get further information. Feel free to delete / edit the table to provide more or less for your students.

## Slide 29: Focused Tasks
During the exploration and development of ‘carrying cargo’, there are a number of focused tasks you could use in this unit of work to support the design process or simply use the context as a vehicle to deliver these particular skills. The following are just some it lends itself well to:
‘Visuals vs function’ | ‘AI visuals’ | ‘Attached canvas’ | ‘Micro carrier’
Use CAD to create early idea concepts and use rendering or AI to visualise the finished product. Make a functional model or prototype and present both to show your vision without spending a long time making a finished prototype. | Using online tools such as Vizcom.ai or iPad apps such as Hypersketch, experiment with generative design and text prompts to visualise your final commercial product using your own sketches and photos of simple models. | Whilst not on e-scooters, bicycles often have the option for a water bottle carrier. Make a new carrier prototype that uses this water bottle mount. Using an attached canvas of a water bottle / other product, design around this for a perfect fit. | Often it’s small items that need carrying – pumps, mobile phones, house keys. Consider using scrap water-proof fabrics to make a simple carrier that connects to the handlebars or similar. Fabric may include old tent fabric / advertising banners or waterproof clothing.
‘Radar charts’ | ‘Screw threads’ | ‘Pricing’ | ‘Metal bottle holder’
Provide (or collect) data for students to create their own radar chart as a way of making a visual judgement. This can be using Excel or similar. | Demonstrate how to add an external screw thread to a bar, allowing it to be screwed into the bottle mount of a bicycle frame, utilising this area for attaching something. | As a class, explore the potential costs of a simple product. This may be a previously made student product. What did the materials cost? What about paying the manufacturer, adding on sales %. What would it cost to sell? | Using wire, create a simple design for a bottle holder for a bicycle. Can a single piece be bent to hold it and then brazed onto a flat to mount to a bicycle. Consider powder coating the final piece.
Notes: Click the titles to access member Focused Tasks and Investigative & Evaluative Activities in detail.

## Slide 30: Image bank
A selection of sketches from Pure Electric. Although not directly linked to carrying cargo, they may be useful to show a range of communication techniques
Notes: The following images may be useful to share with students and/or to use to create additional resources for your work in this unit.

## Slide 31: Image bank
A selection of sketches from Pure Electric. Although not directly linked to carrying cargo, they may be useful to show a range of communication techniques.
Notes: The following images may be useful to share with students and/or to use to create additional resources for your work in this unit.

## Slide 32: Image bank
A selection of sketches from Pure Electric. Although not directly linked to carrying cargo, they may be useful to show a range of communication techniques.
Notes: The following images may be useful to share with students and/or to use to create additional resources for your work in this unit.

## Slide 33: Investigative & Evaluative Activities
The investigate, or research, element of this project should be relatively easy to carry out as scooters and bikes are all around us. However, consider looking at a wide range of personal transport for different uses. See if you can spot opportunities for adding elements to that device without compromising its safety. Think about how you can create something unique from what you discover in your research.
‘Bag analysis’ | ‘CAD testing’ | ‘Material tests’
Looking at bags / holdalls / suitcases can allow for students to know how to carry out research as well as gain valuable inspiration. Consider getting a few varieties of bags / suitcases and carry out a product analysis. Students could deem what is frustrating and beneficial about them. This may be scuffing, storage when empty, ease of use, weight, allowing you to fit in large amounts / awkward shapes etc. | FEA (Finite Element Analysis) is a form of virtual stress testing built into many CAD packages. Using the 3D CAD model from the focused tasks, use the FEA in your CAD package to test the model by applying forces to it. | The cargo system could be a combination of hard and soft materials, but this means there is a wide range of possibilities. What materials are available to you? The context allows an opportunity to explore properties of materials by carrying out a range of tests. Is it water-proof or splash-proof? How can you test durability? What tests / properties are necessary / useful? For example, even when thinking of suitcases, are hard-shells preferable to soft? Lots of discussion point opportunities here.
Notes: Click the titles to access member Focused Tasks and Investigative & Evaluative Activities in detail.

## Slide 34: Empathize tasks
‘Competitor analysis | ‘Consumer research’
Design is big business, and a successful design takes into account the needs of the customer while also being aware of what other products are on the market. Look at the range of products on the market at the moment and ask some of these questions: What is their USP? Discuss what makes that product unique or stand out in the market? Relate this to the context. What product from experience or research stood out as being different or ‘unique’? What was its USP? Make a list of these USP features and use them to define the criteria the student will want to try and incorporate in their designs. What did they cost? Did they offer any other benefits over their competitors? Who is the market leader in this area of products, and why are customers loyal to the brand? You may be able to look at similar products (and bring them in to class) such as cycle baskets, bags that attach to handlebars etc, Internet images are ok, but actual products are always preferable. Consider building up a resource bank and maybe ask your school community to bring some in. | The consumer is the customer, and they will buy the product that you design if it appeals to them and meets their needs. It is important that you consider their needs as you progress. There are two main ways of doing this: Online consumer research Use the internet to look at online stores and their sales. Which products are most popular with good reviews? Post online polls for those members of your target market. You may be able to do this with a link in the school newsletter to get a wide reach. Ask they what they are looking for in a product to carry cargo. In person consumer research You could ask the same questions in person, but you can tailor the interview to the person and ask other questions. Consider observing people travelling to work on bikes and scooters. How are they carrying their cargo? Is there an opportunity to speak to students that arrive at school on a scooter? Do you have an e-scooter scheme near your school? Are you able to observe or speak to users? Consider as many users as you can (Who). What are their particular needs. Remember also that design such be sustainable and inclusive so should focus on being accessible for all users. This may help spark further areas to consider.
Notes: Feel free to edit / use these with your class as appropriate. Change the wording and share with students if you wish, or use to help your own planning.

## Slide 35: Define tasks
‘Viability’
Getting students to look at the viability of their ideas can be a good way to incorporate elements of maths and business. The potential size of the market may be through some research. Whilst they are unlikely to find exactly how many people ride e-scooters and wish to carry groceries on it, by looking at the 3 ways that Pure mention: Survey existing users Competitor analysis Amount of what people want to carry In addition, looking at the market of e-scooters, and those that regularly cycle / use scooters rather than cars, they may be able to have an educated guess. This will be a good exercise in both research, but also forming conclusions. Similarly, finding out what people would be willing to spend means that students will need to get useful, valid research from people, then look at how to create ‘averages’ based on what is likely to be a range of data.
Notes: Feel free to edit / use these with your class as appropriate. Change the wording and share with students if you wish, or use to help your own planning.

## Slide 36: Define tasks
‘Planning ahead’ | ‘Statement’
Planning is an important aspect of project management when designing. Deadlines need to be met if the product is to be manufacture and distributed on time. Even in a school setting, time management is a key skill. Try using a Gantt chart like the one below to manage the sections of the design project allowing time for several loops of the ideate, prototype, test cycle to explore various iterations. Consider giving the students the main start and end dates as per how much time you are allowing to this project. | We are used to creating product design specifications in D&T where we specify things like aesthetics, cost, durability, function, safety etc, but this ‘statement’ that Pure mentions is more like their USP. Think of it like what you may include in an advertising campaign. When students have a range of ideas (note, at this stage it is more ‘thoughts’ rather than drawn ideas) and are struggling to decide which one(s) to develop further, they may wish to use criteria to grade against, e.g. Aesthetics Appeal Cost Complexity Originality. With these, consider letting students find their own way with grading them. They may not see ‘complexity’ as a positive aspect and choose to use a minus amount. Some may decide that they aren’t all equal in grading, and so some count for double (for example) and so can create an existing discussion. You may wish to get students to rank them firstly in order of importance before progressing with the task.
Week | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12
Investigate |  |  |  |  |  |  |  |  |  |  |  | 
Ideate |  |  |  |  |  |  |  |  |  |  |  | 
Prototype |  |  |  |  |  |  |  |  |  |  |  | 
Test |  |  |  |  |  |  |  |  |  |  |  | 
Implement |  |  |  |  |  |  |  |  |  |  |  | 
Notes: Feel free to edit / use these with your class as appropriate. Change the wording and share with students if you wish, or use to help your own planning.

## Slide 37: Ideate tasks
‘Looks like/works like’ | ‘Competitor and mood board’
When designing a utility item for carrying cargo, it is important that you design a functional item that does the job in an effective way. However, consumers will still be drawn to how a product looks so it is important that your product also looks appealing. Your look like ideas can be sketches and rendered images or they could be CAD models. These will allow you to focus on: Aesthetics, with the focus on form, colours materials, graphics etc. Simple functions such as how something folds up or operates Works like will allow you to physically interact with aspects of the design such as: Scale and proportion. An image on screen will not always convey the weight, scale and proportion. Ergonomics. Interacting with an object can only be experienced and evaluated in person. Assembly and fittings. It is easier to show where parts fit together or how they move or operate when you can physically move them, Interaction with other elements. CAD models do not have real solid materials so they can be ‘put together’ in ways that might not work in the real world. Students may create a rough prototype, using scrap fabrics, mis-matching fastenings etc, that they are able to test and prove a concept. However, they may have an accompanying CAD render or drawing that shows how it may look ideally. This could have logos, fastenings etc. | We all need inspiration when designing new products, especially if the product is quite new and unique. Use the internet, magazines and brochures to collate images of competitor products, even if they don’t exactly match the intended function. Get students to make a mood board where they highlight the key aspects of the design that work for their needs. These could be cost, materials, function or anything that inspires them. Don’t be afraid to look outside of the area of focus as sometimes a product designed for a completely different purpose might offer inspiration. Try look at travel luggage such as suitcases, utility items such as tool-boxes and even camping equipment for its light weight and portability. You could also create a mood board with other imagery that will help you visualise your ideas. This could be rockets, animals, colours, material combinations, shapes, or anything you feel will inspire your own creations. Often students will happily throw images down with little consideration. You may want to get them to make a brief note on each addition. As per Pure, is it something they like, something they wish to avoid, or a gap in the market. Consider splitting into 3 and having all three elements in columns on the same page.
Notes: Feel free to edit / use these with your class as appropriate. Change the wording and share with students if you wish, or use to help your own planning.

## Slide 38: Ideate tasks
‘Try them out’ | ‘Ideate vs prototype’
It is unlikely that you will be able to get hold of cargo carrier for e-scooters (yet!) and so asking the school community for examples for bicycles, cars (think about inside the car), motorbikes and more may be useful. There is also the opportunity to purchase them very low-cost on Facebook Marketplace and other similar places, to build up a handling collection. Get students to actually use them as intended. Put items in them, fasten them to the handlebars, ride around the playground with them. They may even wish to use them for a week and provide feedback afterwards. Consider giving them (or generating as a class) criteria to judge them against. You may wish to use a radar chart or similar (one of the Focused Tasks) to rate them. Experience has shown us that students use internet-based research a lot, and so this primary research and product handling is a vital way to analyse products and draw out information from existing products that they may wish to use in their own work. | Getting students to iterate can be tricky. You may wish to try and structure this initially, to ensure they don’t simply run with their first idea, they don’t omit testing elements (such as checking the size, ensuring the fastening works…) You could do this in a number of ways, getting students to use coloured dots or similar to indicate different stages e.g. red for design, blue for a test. You may wish to split designs into key aspects – so the students design fastenings first, then test them, then move onto the storage body, and test them, then how to open/close… As mentioned in the video, consider having to hand, a wide range of materials such as card, wire, foam to ensure it is a true representation of how Pure Electric work when creating ideas.
Notes: Feel free to edit / use these with your class as appropriate. Change the wording and share with students if you wish, or use to help your own planning.

## Slide 39: Prototype tasks
‘Cut and shut’ | ‘Increased resolution’
Materials are expensive and it is also time consuming to develop prototypes from scratch. To speed up the process, you can use a ‘cut and shut’ approach. This involved taking existing parts and components and joining them together. Using existing components, ideally broken, obsolete, or unwanted, stick and glue the parts together to create your own designs. You may want to use existing hardware from bikes or scooters such as racks, bags and panniers. This is useful when making a fabric prototype as you can quickly cut and stick or sew fabric pieces as well as using straps, catches, fasteners, zips etc. Don’t worry If you are limited to the materials or products available. This can also be done visually using a computer to make a collage of different parts to create a new design without the need to draw all the details. Try these various ‘cut and shut’ approaches to quickly prototype ideas in the early stages of development to save time and materials. To help with this, have a range of fastenings, materials and components available for students to utilise in their designs. They may wish to photograph them, or draw them once modelled. Other students can then use the parts if required. From this photo you could even use AI to develop the crude model further. | As per the method of Pure Electric, it can be useful to get students to understand when to spend time and energy on a design, and when not to. To help with this, time limits could be set on various aspects of the design, which in turn force lower, or higher resolution. For example, initial ideas / sketches may be limited to 30 seconds per idea. The time can then be increased on later ideas. It may be worth explaining this concept, and the fact that perfect drawings / beautiful models aren’t required early on (or indeed a good use of time) whilst you are feeling your way through an idea. You could draw on other disciplines such as music, art, storyboarding a film, when the ideas may be a brief hummed melody, a quick stick-man figure or sketchy storyboard before developing it little by little as it progresses.
Notes: Feel free to edit / use these with your class as appropriate. Change the wording and share with students if you wish, or use to help your own planning.

## Slide 40: Prototype tasks
‘Aspirational model vs functional model’
Consider the purpose of creating a prototype. Is it to check the aesthetics, scale, proportion etc. or is it to test functionality and how it can actually be used by a person? An aspirational model is what you would like the finished product to look like. This sort of visual prototype may be more concerned with aesthetics; how it looks. These can be useful in selling the concept of a product to potential customers as well as to your client. Use CAD software to render out realistic looking visuals in different materials and finishes. Place your CAD model in a virtual environment on screen, or using AR. Advances in generative AI allow you to see what a simple sketch would look like as a finished product and can even produce visuals from just a written description. Explore all of these tools when trying to visual the finished product. A functional model is more concerned with how the product works and it may look almost nothing like the finished product. This could be a quickly built test rig to see how a particular function works or for fatigue testing. It may be a scale model with a full-size working element that can be operated and tested such as a catch or lock. Remember that the two work together during product development, and your final proposal could be a working model and a visual of the finished product.
Notes: Feel free to edit / use these with your class as appropriate. Change the wording and share with students if you wish, or use to help your own planning.

## Slide 41: Test tasks
‘CAD tests’ | ‘Real material tests’
Again, the use of modern CAD software brings a wealth of benefits including the ability to virtually ‘test’ your CAD models. As well as being able to test the visual aspects of your design through photorealistic rendering, animations and flythroughs, most software will have some aspect of FEA available. FEA allows you to specify the materials or components your design is intended to be made from, and the software calculates the mass, density, strength, elasticity etc. You can set fixed points where the model cannot move such as the points where it fixes to your bike or scooter. You then specify the force being applied to parts of the model and how much load it being applied. The simulation will then run and show you where the strongest/weakest point would be and where they are likely to fail. You can then edit the model and rum the simulation again to see if you have made improvements. Repeat until you are happy with the results. Refer to the tutorials and instructions available with the software you are using or the supporting and curriculum units available with these contexts for further support. | Virtual test may be physically accurate based on the data provided, but they will not be the same as actually interacting with real materials. Equipment to test materials accurately will be expensive, but you can still get samples of materials and see how they feel to handle. Put a material sample under a load and see how they react Try exposing them to elements such as heat and cold to see how they react. Apply water under pressure to simulate heavy rain Which materials offer the greatest flexibility to be carried or packed away when not in use? Consider making two prototypes: one to test with your target market for feedback, and another to test to destruction.
Notes: Feel free to edit / use these with your class as appropriate. Change the wording and share with students if you wish, or use to help your own planning.

## Slide 42: Implement tasks
‘Target cost’ | ‘Bill of materials’ | ‘Price points’
A proposed product will always have competitors on the market who may offer more features, a lower price or both! It is important that your target cost takes into account the type of product you are aiming for (low-cost vs premium) and that there is a market for this type of product. Would you pay a high price for a soft bag or a suitcase? What unique features might your product have that would make it stand out in the market. If two products were the same price, what would persuade customers to by one over the other? If your design were more expensive, what would it offer for the extra cost? It is also important to use your research to be sure there is a market for your product and that it is designed to meet the target cost. Use your customer and competitor research to decide on a target cost for your product. | A bill of materials is used to create a list of parts and components in a product. This can also be used to create a cost price for the materials to manufacture the product or prototype. In industry, these will be linked to the prices of those parts so the manufacturer can see if these will affect the cost of the product. After Covid we saw the prices of materials increase dramatically and the lack of electronic components drove up the price of technology-based products. If using CAD to create a model or assembly, a working drawing can be produced which will often generate a bill of materials. Alternatively, you can use a spreadsheet to list the parts needed and their costs, to see the total cost of the product. | Here is where the bill of materials can show if the product will be affordable for the consumer and profitable for the manufacturer. Products often sell for around 3 times what they cost to make to cove, storage, marketing, distribution, shipping and retail profit etc. If you are making a premium product, it could cost you £50 to make it, but would the customer pay £150 for it. At the other end of the scale, you might design a low-cost DIY kit that costs just £5 to make and sells for £15, but it would not be considered a premium product. Could you aim for something in between the two? What would need to change to allow this? There is often a deal of compromising in design…
Notes: Feel free to edit / use these with your class as appropriate. Change the wording and share with students if you wish, or use to help your own planning.

## Slide 43: Level of challenge
Design contexts increase in challenge for each of the KS3 years. By reducing the scaffolding and support you can develop opportunities for more individual and innovative work to be produced.
Closed
Task
Open
Task
Context with Brief
Supported Context
Open Context
Simple solution made from existing parts ‘cut and shut’ together to make a working prototype. Items to hold can be prescribed, as with the materials.
Greater variety of materials and techniques shared. Possibly options of the routes to take e.g. holder for a phone, holder for a lunch box. Outcomes may include from-scratch designs.
A complete and working prototype that can be fully tested. An open brief for the items to be carried and fully-working outcomes expected. A variety of materials and processes available to choose from.
Notes: Suggested levels of challenge. Use these for reference and set your own aims and objectives for the contexts.