## Slide 1: James Webb Space Telescope
A STEM into Action resource
funded by the UK Space Agency
  In the context of constructing an astronomical telescope and studying the James Webb Space Telescope, improve pupils’ understanding of space history, technology and the uses of observational data
Notes: These materials are aimed at teachers of STEM subjects in secondary schools.
Funding and support was provided by the UK Space Agency.
Development of materials was managed by the Design and Technology Association.

## Slide 2: Outcomes
Improve pupils’ understanding of space through:
  Awareness of optical telescopes and how they developed
  Understanding how our knowledge of the Universe has developed
  Understanding the design and operation of the James Webb Space Telescope (JWST)
  Telescope design and manufacture
  Using telescopes
Notes: The project booklet guides pupils through a series of exercises that:
Explain how observation of the night sky has developed and improved our understanding of the Universe
Raise awareness of the James Webb Space Telescope, how it will operate, and UK involvement
Improve pupils’ understanding of telescope design and manufacture by them making and testing their own low-cost telescope

## Slide 3: Astronomy
Building astronomical telescopes
Making observations
Aware of objects in the night sky
Earth in our Galaxy
Our Galaxy in the Universe
STEM
Notes: Building and using your own astronomical telescope is a great way of gaining an awareness of the night sky and space observation.
Amateur astronomers use a wide range of commercial and home-made equipment to view and capture images of objects in the Universe visible to people on earth.

## Slide 4: Working in teams – Ages 11-14
Astronomical telescope
Bi-convex lenses
Card or plastic tubes
Disc spacer
STEM
Notes: Even telescopes made from low-cost materials and plastic lenses will let you see objects on Earth and in the night sky in greater detail.

## Slide 5: The first telescopes
1608 - Early Dutch telescopes
Scientists including Englishman Thomas Harriot viewing objects in the night sky
Italian Galileo Galilei recognised as the first to use a telescope for astronomy
Galileo’s telescope had a magnification of 3x
https://en.wikipedia.org/wiki/Galileo_Galilei
STEM
Notes: Scientists were using lenses to create telescopes as early as 1608 including Englishman Thomas Harriot (also spelled Harriott, Hariot, or Heriot) who used a Dutch telescope to view the moon.
Italian Galileo Galilei is recognised as the first person to use a telescope for astronomy in 1609.
Galileo’s telescope had a magnification of 3x. He used a bi-convex lens for the objective and a bi-concave lens for the eyepiece causing viewed objects to appear the correct way up.

## Slide 6: Refracting telescopes
Parts of a telescope
STEM
Notes: Optics is the branch of physics which involves the behaviour and properties of light, including its interactions with matter and the construction of instruments that use or detect it.
Small, low-cost telescopes have two lenses, a larger ‘objective’ lens and smaller ‘eyepiece’ lens.
The person viewing a distant object focuses the image by altering the distance between the two lenses.
The telescope on the right has a rack and pinion gear moving the rear tube providing fine adjustment of the focus.

## Slide 7: Bi-convex lenses
Refractive index – lens material
Refraction – light is deflected on entering and leaving the lens
Curvature – determines where the light rays focus
Focal point – where light rays converge
STEM
Notes: Prisms
In science lessons you perform experiments to show how light rays passing through angled glass prisms change direction.
Refraction
Light travels through air and other transparent materials at different rates. This causes the light to be deflected or ‘refracted’ at the intersection between them.
Bi-convex lens
The refractive index of the glass and radius of curvature determines how much the light will change direction. Light from distant objects enters the lens and, where this is at an angle to the glass, the light is refracted. The curved lens surfaces cause light rays from a distant object to converge at a single ‘focal point’.

## Slide 8: Lens manufacture – Plastic
Thermoplastic polymer
  Acrylic
  Polycarbonate
Optically clear
Injection moulded
High volume
Low cost
https://www.youtube.com/watch?v=b1U9W4iNDiQ
STEM
Notes: Low-cost lenses are made from optically clear thermoplastic polymers including polycarbonate and acrylic.
Injection moulding allows high volume production which keeps the unit cost of each lens very low.
Follow the link to watch a video explaining how injection moulding machines work.

## Slide 9: Lens manufacture – Glass
Optical glass
Cast blank
Cutting, grinding, polishing
Low-medium volume
Mid-high cost
https://www.youtube.com/watch?v=hX_YH0p_q9A
STEM
Notes: Most high quality lenses are made from optical glass by several processes including cutting, grinding and polishing.
Follow the link to watch a video showing lenses being manufactured.

## Slide 10: Sourcing lenses
Re-use from old magnifiers
  Must seek permission first!
Suppliers to schools
  Rapid Electronics
  https://www.rapidonline.com/catalogue/search?Query=convex%20lens&Tier=Lenses
  Breckland Scientific
  https://www.brecklandscientific.co.uk/
  Phillip Harris
  https://www.philipharris.co.uk/search?phrase=lens
STEM
Notes: Make sure you get permission before dismantling magnifiers for their lenses!
Lenses can be removed from old magnifying glasses and jewellers’ loupes.
Opticians often sell magnifying glasses and jewellers’ loupes.
Lenses can be purchased from different suppliers.
Rapid Electronics, Breckland Scientific and Phillip Harris are three UK suppliers of STEM resources for schools and their catalogues list a range of bi-convex lenses.
https://www.rapidonline.com/catalogue/search?Query=convex%20lens&Tier=Lenses
http://www.brecklandscientific.co.uk/OLE-350-300-p/ole-350-300.htm
https://www.philipharris.co.uk/search?phrase=lens

## Slide 11: Finding the focal length of a lens
Lens and card on a ruler
Facing the window
Move lens to focus the image coming through the lens onto the card
Distance on ruler = focal length (FL)
STEM
Notes: Set up your lens like the photograph here facing light coming through a window.
The lens can be clamped or held by Blu Tack.
A vertical piece of paper on a wall or box will act as a screen for the image.
The ruler zero mark should be aligned with the paper screen.
Move the lens towards/away from the paper screen until the image of the window is in sharp focus.
Make a note of the distance between the screen and the lens.
This is the focal length for that lens.
Repeat the experiment for the eyepiece lens.
Result of the experiments in the guide:
Focal length (objective) = 205 mm
Focal length (eyepiece) = 75 mm

## Slide 12: Magnification
For these lenses:
Objective lens FL = 300 mm
Eyepiece lens FL = 50 mm
STEM
Notes: Knowing the focal length of your lenses, it is possible to calculate the magnification for your telescope.
Magnification = focal length of objective lens focal length of eyepiece lens
Example 1
Using focal lengths from the lenses above:
Magnification = 205 = 2.7 75
Written as 2.7x magnification
Example 2
Using lenses with focal lengths of 1000mm (objective) and 40mm (eyepiece)
Magnification = 1000 = 25 40
Written as 25x magnification
You should now be able to pair up lenses, choosing the focal lengths to give a specific magnification.
Higher magnifications combine a long focal length objective lens and short focal length eyepiece lens.
Magnification is only one consideration; equally important is the brightness of the image. This is determined by the diameter of the objective lens and how much light it can capture.
The image seen through a telescope with a high magnification but small objective lens is likely to be dull and unclear.

## Slide 13: Tube length
Lenses FL = 300 mm and 50 mm
Tube overlap = 100 mm
Lens distance
Tube lengths
STEM
Notes: The lenses need to be positioned in a telescope with their focal points in the same position.
Allowing for a reasonable overlap between the tubes provides movement either side to focus the image.
Example:
With these lenses:
Objective lens focal length = 300 mm Eyepiece lens focal length = 50 mm
Lens distance = 300 + 50 = 350 mm
If you want an overlap of 100 mm and both tubes are the same length, how long will the tubes need to be?
Example:
Half the overall length + half the overlap
175 mm + 50 mm
So, both tubes need to be 225 mm long.

## Slide 14: Sliding tubes
Tubes must slide smoothly
Changing the diameter of tubes
STEM
Notes: Reducing tube diameter
We could cut narrow strips lengthwise out of a tube until we achieve the required diameter but a more structured approach will be more accurate.
A knowledge of geometry lets us achieve an accurate outcome much quicker.
Using measurements from the first tube:
A 13mm strip needs to be cut down the tube to reduce the outside diameter from 84mm to 80mm.
Pupils will need to repeat these experiments and calculations for the diameter of their tubes/lenses.
Reducing tube diameter
We could cut narrow strips lengthwise out of a tube until we achieve the required diameter but a more structured approach will be more accurate.
A knowledge of geometry lets us achieve an accurate outcome much quicker.
Using measurements from the first tube:
𝐶𝑖𝑟𝑐𝑢𝑚𝑓𝑒𝑟𝑒𝑛𝑐𝑒=𝑝𝑖 𝑥 𝑑𝑖𝑎𝑚𝑒𝑡𝑒𝑟
𝐶=3.142 𝑥 84 𝐶=3.142 𝑥 80
𝐶=264 𝑚𝑚 𝐶=251 𝑚𝑚
𝑫𝒊𝒇𝒇𝒆𝒓𝒆𝒏𝒄𝒆=264−251=𝟏𝟑𝒎𝒎
A 13mm strip needs to be cut down the tube to reduce the outside diameter from 84mm to 80mm
Pupils will need to repeat these experiments and calculations for the diameter of their tubes/lenses.

## Slide 15: Sliding tubes
Analysis in Autodesk Inventor
  Activate the Analysis tab
  Measure group > Loop
  Select the edge
  The measurement is displayed
STEM
Notes: CAD analysis
Computer modelling offers an alternative to mathematical calculation.
CAD software can be used to measure the dimensions of objects including circles and cylindrical shapes.

## Slide 16: Cutting and joining tubes
Marking out
Cut using craft knife/safety rule or fine tooth saw
Elastic bands while glue sets
CRAFT KNIFE
SAFETY RULE
GENT’S SAW
STEM
Notes: Risk assessments must be carried out with control measures followed at all times.
Before using any workshop tools, pupils must be shown how to use them safely and supervised when carrying out the process.
Mark out two lines showing where the segment needs to be cut out. A straight edge made from angled section makes drawing lines parallel to the axis of tubes easy.
Multiple cuts with firm pressure using a craft knife against a safety rule will cut through thin card tubes.
Make sure the tube is held securely for cutting. You could rest the tube across the open jaws of a woodworking vice.
Thicker card and plastic tubes are best cut using a fine tooth saw designed for cutting wood and soft plastics. A Gent’s back saw with very fine teeth is ideal for this. If you don’t have a Gent’s back saw, you could use a dovetail or Tenon saw.
When checking the tubes slide smoothly, use elastic bands to hold the edges together.
Use an appropriate adhesive to glue the cut edges together.
Use elastic bands to hold the edges together while the adhesive sets.
Cut a disc the correct size to hold the eyepiece lens in the end of the smaller diameter tube.
Glue the lens into the hole in the disk. Make sure you keep glue away from the surfaces of the lens.
Glue the disk into the end of the smaller tube. Depending on the materials, electrical tape may be appropriate for this joint.

## Slide 17: Assembling the telescope
Tape objective lens into larger tube
Glue eyepiece into spacer disk
Glue disk into smaller tube
Check tubes slide smoothly
STEM
Notes: Glue the objective lens into the end of the larger tube. Electrical tape may be suitable for this joint.
Slide the smaller tube inside the large one with the lenses at the outer ends.
Check the tubes slide smoothly.

## Slide 18: Testing
Design tests to assess the performance of your telescope
Carry out those tests
Record the results
Report on the benefits and limitations
Suggest improvements including:
  Materials
  How parts would be made
  How the changes would work and how they would improve performance
STEM
Notes: Using the knowledge you have gained, design tests to measure the performance of your telescope.
Carry out the tests, recording the results.
Create a report outlining the benefits and limitations of your telescope.
Add a section to your report suggesting improvements to the design.
Sketch the changes adding notes explaining:
  the materials that could be used and the properties that make them suitable.
  how the parts would be made.
  How the modifications would work.
Describe how these changes would improve the performance of your telescope.

## Slide 19: Testing
Focus the telescope at a distant object such as a tree
Open your other eye to view the tree directly
Estimate the difference in size for the magnification
STEM
Notes: HIDDEN SLIDE
Use this slide if pupils struggle to find ways of testing their telescopes.

## Slide 20: James Webb Space Telescope (JWST)
Launch set for June 2019
Aims to improve our understanding of the Universe
Looking at infrared radiation
Sails shelter the telescope and instruments from the Sun
Instruments cooled to almost absolute zero (-273oC)
STEM
Notes: The James Webb Space Telescope is due to launch in June 2019 and has been designed to find evidence that will extend our understanding of the Universe is several areas.
It will be used to study the first stars and galaxies by looking at the infrared spectrum.
To achieve this the instruments must be cooled to within a few tens of degrees above Absolute Zero or - 273°C. This is to prevent radiation from the telescope and its instruments swamping the faint and distant astronomical signals.

## Slide 21: UK involvement in the JWST
Government funding through STFC
UK Astronomy Technology Centre
  Royal Observatory, Edinburgh
Mid Infrared Instrument (MIRI)
20+ partners including:
  Rutherford Appleton Laboratory
  Astrium Ltd
  University of Leicester
  https://www2.le.ac.uk/departments/physics/research/src/res/mech_eng/present-missions/miri-project
STEM
Notes: The Science and Technology Facilities Council (STFC) is a UK government body that carries out civil research in science and engineering, and funds UK research in many areas including space science and astronomy.
The STFC funds the UK Astronomy Technology Centre (UK ATC) with headquarters at the Royal Observatory in Edinburgh. They design and build instruments for many of the world's major telescopes including the Mid Infrared Instrument (MIRI) for the JWST.
More than 20 partners are developing MIRI including the Rutherford Appleton Laboratory, Astrium Limited, the University of Leicester.

## Slide 22: UK involvement in the JWST
UCL – Mullard Space Science Laboratory
  Calibration and NIRSpec
UCL + Astrium
  JWST
  Gaia, ESA mapping the Galaxy
STEM
Notes: University College London’s Mullard Space Science Laboratory helped with the development of the on-board and ground calibration equipment and another sensor on JWST, the Near Infrared Spectrometer (NIRSpec).
UCL has partnered with Astrium on several contracts including the JWST and Gaia, ESA’s next generation astrometry mission to map the Galaxy, which launched in December 2013.
http://www.ucl.ac.uk/impact/case-study-repository/supporting-the-growing-uk-space-sector

## Slide 23: UK involvement in the JWST
Tekdata Interconnect Systems (Staffordshire, UK)
Cryogenic harness
Linking JWST’s major systems
https://www.tekdata-interconnect.com/blog/drive_me_to_the_moon.asp
STEM
Notes: University College London’s Mullard Space Science Laboratory helped with the development of the on-board and ground calibration equipment and another sensor on JWST, the Near Infrared Spectrometer (NIRSpec).
UCL has partnered with Astrium on several contracts including the JWST and Gaia, ESA’s next generation astrometry mission to map the Galaxy, which launched in December 2013.
http://www.ucl.ac.uk/impact/case-study-repository/supporting-the-growing-uk-space-sector

## Slide 24: Interactive 3D model of JWST
Follow the link below to learn more about the JWST through an interactive 3D model
https://jwst.nasa.gov/Webb3d/#
STEM
Notes: Follow the link below to learn more about the JWST through an interactive 3D model.
https://jwst.nasa.gov/Webb3d/#
Note: The interactive model requires Java so will not work with the Google Chrome or Microsoft Edge browsers. Paste the link into Firefox or Explorer.

## Slide 25: Careers in UK Space Programmes
1000s of people working on JWST
Three partner organisations:
  NASA
  ESA
  Canadian Space Agency
Meet the JWST team
https://jwst.nasa.gov/meettheteam.html
Professor Gillian Wright Director, UK Astronomy Technology Centre Royal Observatory, Edinburgh
STEM
Notes: A great many people are involved in designing, building and preparing the JWST across three partner organisations; NASA, ESA and the Canadian Space Agency.
https://jwst.nasa.gov/meettheteam.html

## Slide 26: Amateur astronomy
British Astronomical Association
https://www.britastro.org/
The Royal Astronomical Society
http://www.ras.org.uk/
The society for popular astronomy
http://www.popastro.com/main_spa1/
STEM
Notes: Amateur astronomy
A number of organisations support amateur astronomy in the UK including:
The British Astronomical Association - https://www.britastro.org/
The Royal Astronomical Society - http://www.ras.org.uk/
The society for popular astronomy : http://www.popastro.com/main_spa1/

## Slide 27: Locating celestial objects
The Earth is rotating
Stars and planets appear to move in the sky
A system of coordinates is needed to ‘map’ objects
Star Walk 2 – Augmented Reality App
http://www.vitotechnology.com/star-walk-2-guide-sky-night-day.html
STEM
Notes: When you look up at the night sky you are seeing the Universe from a rotating planet, the Earth.
Looking up at the night sky on a clear night we see a constantly moving panorama of celestial objects.
To keep a celestial object in view, the telescope must be constantly moving and an understanding of 3D geometry will help when locating objects and following their movements.
Star Walk 2 is available for the main mobile phone operating systems. It is an augmented reality app that overlays information about objects in the sky while viewing it live.

## Slide 28: Geometry – Cartesian coordinates
Cartesian coordinates are named after 17th Century French scientist Rene Descartes
Cartesius is Latin for Descartes
Three perpendicular axes x, y, z
Any point in space has coordinates
Coordinate on right is 5,4,3
Most CAD software uses this system
STEM
Notes: In mathematics you have learned about graphs, axes and coordinates.
Two dimensional graphs have x and y axes and any point on the graph can be described with x and y values. The numbers representing a point on a graph are called coordinates.
Add a third axis at right angles to the x and y axes and you have a 3D graph. This system can also be used to locate points in 3D space.
The point in the diagram has a 3D coordinate of 5,4,3.
These are called Cartesian coordinates, named after the 17th century French philosopher, mathematician and scientist, Rene Descartes. ‘Cartesius’ is a translation of the Latin ‘Descartes’.
Most 3D modelling software uses Cartesian coordinates to calculate the position of geometry in the virtual workspace.

## Slide 29: Geometry – Polar coordinates
Polar coordinates use distance and angle
Origin is at 0,0
Angle reference is East with angles measured anticlockwise
Distances from origin
The two points here are:
  5, 30o and 3, 225o
STEM
Notes: An alternative method of plotting the position of objects on a 2D plane uses angles and distances.
These are called polar coordinates.
Two examples are shown in the diagram:
5, 300
3, 2250
Early 2D CAD software defined the horizontal line to the right of the origin as the reference for angles measured anticlockwise.

## Slide 30: Latitude and longitude
Early geographers devised the system we use today
Latitude angle Ø is measured north or south from the equator
Longitude angle λ is measured East or West from the Greenwich meridian
London lat/long 51.5074° N, 0.1278° W
Tokyo lat/long 35.6895° N, 139.6917° E
Sydney lat/long 33.8688° S, 151.2093° E
https://en.wikipedia.org/wiki/Latitude
STEM
Notes: How do we know where we are on the surface of the earth?
Early geographers devised a system using angles for latitude Ø (measured north or south from the equator) and longitude λ (measured east or west from the Greenwich meridian)
Latitude and longitude coordinates locate position on the surface of the earth.

## Slide 31: Ascension and Declination
Ascension is equivalent to longitude
  Measured in hours (h) minutes (m) and seconds (s) with 24 hours equivalent to 360 degrees
Declination is equivalent to latitude
  Measured in degrees °, arc minutes ‘ and arc seconds “.
  North of the celestial equator is positive
  South of the celestial equator is negative
STEM
Notes: Astronomers use a system similar to latitude and longitude when recording position of celestial objects in the sky.
Ascension is equivalent to longitude and is Measured in hours (h) minutes (m) and seconds (s) with 24 hours equivalent to 360 degrees.
Declination is the equivalent of latitude and uses the units of degrees °, arc minutes ', and arc seconds ".
Declination north of the celestial equator uses +ve values with –ve values being used for points south of the celestial equator.
https://en.wikipedia.org/wiki/Declination

## Slide 32: Ascension and Declination
Sirius A is the brightest star in the night sky and has coordinates
  Right Ascension: 06h 45m 08.9s
  Declination: -16° 42’ 58”
STEM
Notes: Sirius A is the brightest star in the sky and has coordinates:
  Right Ascension: 06h 45m 08.9s
  Declination: -16° 42’ 58”

## Slide 33: Electromagnetic spectrum
Describes the radiated energy around us
Energy travels as waves
Measured as wavelength or frequency
We see visible wavelengths
JWST looks in the Infrared wavelength
STEM
Notes: The electromagnetic spectrum describes the radiated energy that is all around us from very short wavelength Gamma radiation at one end to Long wavelength waves at the other.
The diagram below shows the broad spread of the EM spectrum and expands the area around visible light.
Visible and infrared wavelengths are the area of interest on this graph.
The orange line in the graph shows wavelengths the human eye is sensitive to. Notice how responsive it is at its peak.
The blue line in the graph shows how an IR blocking filter allows only visible wavelengths through to the sensor.
The red line on the graph shows the sensitivity of the S306 infrared pass filter.
CMOS camera sensors, shown here with a green line, are about half the sensitivity of the human eye but can detect a much wider range of wavelengths.

## Slide 34: Electromagnetic spectrum
Humans see visible wavelengths
  Notice the black plastic bag stops us seeing the hands
JWST is designed to record in the infrared range
  Infrared passes through some materials including clouds
http://www.spitzer.caltech.edu/images/2154-sig08-004-Hands-in-a-Bag-color-Visible-vs-Infrared-Light
STEM
Notes: To properly represent what humans see, digital cameras have an infrared blocking filter fitted immediately in front of the sensor.
The top image was taken with an infra-red blocking filter and displays visible light.
Infrared photography uses an infrared pass filter that cuts out visible wavelengths.
The lower image was taken with an infra-red pass filter and displays infrared light.
http://www.spitzer.caltech.edu/images/2154-sig08-004-Hands-in-a-Bag-color-Visible-vs-Infrared-Light

## Slide 35: JWST Instruments
Located in the Integrated Science Module (ISIM)
This image is from a computer model of the ISIM
STEM
Notes: The James Webb Space Telescope has four main instruments.
These instruments are located in the Integrated Science Instrument Module (ISIM) and at the heart of each one are the sensors.
The diagram is from 3D computer model of the ISIM showing the location of the four main instruments.

## Slide 36: JWST instruments – NIRCam
Near-Infrared Camera (NIRCam)
JWST’s primary imager
Operates in the wavelength range from 0.6 to 5 μm
Two, nearly identical, fully redundant modules
Each has a pair of sensors detecting short and long wavelengths
https://jwst.stsci.edu/instrumentation/nircam
STEM
Notes: The Near-Infrared Camera (NIRCam) is JWST’s primary imager and operates in the wavelength range from 0.6 to 5 μm.
It consists of two, nearly identical, fully redundant modules. Each module has a pair of sensors detecting short and long wavelengths.
https://jwst.stsci.edu/instrumentation/nircam

## Slide 37: JWST instruments – NIRSpec
Near-Infrared Spectrograph (NIRSpec)
Spectrometer working at near infrared wavelengths of 0.6 to 5.3 microns
Spectrographs tell us the intensity of the light coming from objects
Studying spectra tells astronomers many things about celestial objects including: materials – how hot they are and how fast they are moving
http://sci.esa.int/jwst/45694-nirspec-the-near-infrared-spectrograph/
STEM
Notes: JWST's Near-Infrared Spectrograph (NIRSpec) is a near-infrared (wavelengths of 0.6 to 5.3 microns) spectrometer.
Spectrographs tell us the intensity of the light coming from objects at different wavelengths.
Studying spectra can tell astronomers many things about a celestial object, including what they are made of, how hot they are, and how fast they are moving.
http://sci.esa.int/jwst/45694-nirspec-the-near-infrared-spectrograph/

## Slide 38: JWST instruments – MIRI
Mid-Infrared Instrument (MIRI)
Provides imaging at wavelengths between 5 and 28.5 microns
MIRI’s scientific goals include:
  Direct imaging and spectroscopy of young exoplanets and their atmospheres
  identifying and characterising the first galaxies in the Universe
  Probing warm dust and molecular gas in young stars and protoplanetary disks
http://www.backstagescience.com/videos/MIRI.html
STEM
Notes: The Mid-Infrared Instrument (MIRI) provides imaging and spectroscopic observing modes covering the wavelength range from 5 to 28.5 micron.
MIRI’s scientific goals include, but are not limited to,
direct imaging and spectroscopy of young exoplanets and their atmospheres
identifying and characterising the first galaxies in the Universe
Probing warm dust and molecular gas in young stars and protoplanetary disks.
http://www.backstagescience.com/videos/MIRI.html

## Slide 39: JWST instruments – Near InfraRed Imager & Slitless Spectrograph NIRISS
Fine-guidance camera
Wide-field spectroscopy
NIRISS contributed to all JWST Science Themes:
  Looking 13.5 billion years back in time
  The assembly of galaxies
  The birth of stars
  Planetary systems and the origin of life
STEM
Notes: This instrument is packaged with the fine-guidance camera and is capable of wide-field spectroscopy.
NIRISS is poised to contribute to all of the JWST Science Themes:
Looking 13.5 billion years back in time
The assembly of galaxies
The birth of stars
Planetary systems and the origin of life

## Slide 40: JWST operation
Light beams are directed to the different instruments in the JWST using mirrors
The light is reflected from the primary mirror to the secondary one, then through the optics assembly where fine steering mirrors reflect and split the light and direct it to the science instruments by pick-off mirrors
STEM
https://www.youtube.com/watch?v=y9Z2GbFJWmo
Notes: An animation showing redirected light is at: https://www.youtube.com/watch?v=y9Z2GbFJWmo

## Slide 41: JWST operation
JWST being tested
https://www.youtube.com/watch?v=ASbkxmacK-4
STEM
Notes: To give you an idea of how big the JWST is, watch a video of it being tested at NASA’s Goddard Space Flight Centre in Maryland, USA.
https://www.youtube.com/watch?v=ASbkxmacK-4

## Slide 42: JWST bandwidth
JWST Bandwidth = 500 – 5000 nm
5000
STEM
Notes: You were shown this diagram of the electromagnetic spectrum previously.
The James Webb Telescope is designed to record radiation in the range 500 – 5000 nm.
Using this information, pupils should draw a new line on the graph to represent the bandwidth of the JWST.
The purpose of this is not the sensitivity curve of the instruments but the wide operating bandwidth of the JWST compared with the human eye.

## Slide 43: JWST bandwidth
JWST Bandwidth = 500 – 5000 nm
5000
500-5000 nm bandwidth
STEM
Notes: You were shown this diagram of the electromagnetic spectrum previously.
The James Webb Telescope is designed to record radiation in the range 500 – 5000 nm.
Using this information, pupils should draw a new line on the graph to represent the bandwidth of the JWST.
The purpose of this is not to accurately map the sensitivity of the instruments on the JWST but to gain an awareness of the operating bandwidth compared with the human eye.

## Slide 44: Extended projects – Ages 14+
Reference guide
Aimed at pupils engaged in extended projects
Suggestions and links for further investigation and study
STEM
Notes: This section provides older pupils engaged in extended projects with suggestions for further investigation and study.

## Slide 45: Refracting telescopes – Chromatic aberration
Noticeable as blurring and rainbow effects around the edge of objects
Occurs when light passes from the air into a lens and out again
Caused by colours of light travelling at different speeds
https://en.wikipedia.org/wiki/Chromatic_aberration
STEM
Notes: If you have been following this guide from the beginning, you will have built your own telescope using two bi-convex lenses.
You may have found it difficult to get a sharp image and noticed blurring and rainbow effects around the edge of objects.
This is called chromatic aberration and happens when light passes from the air into the lens and out again.

## Slide 46: Chromatic aberration – Seeing it
Science experiment uses a narrow beam of light passing through a triangular prism
White light is split or ‘dispersed’ into different colours
http://microscopy.berkeley.edu/courses/TLM/optics/chromatic.html
STEM
Notes: In science you will have carried out an experiment using a beam of light and a triangular prism.
This clearly shows the way white light is split or ‘dispersed’ into different colours.
http://microscopy.berkeley.edu/courses/TLM/optics/chromatic.html

## Slide 47: Chromatic aberration explained
Like driving a car from a tarmac road at an angle onto sand
First tyre onto sand slows down turning the car slightly
Once all tyres are on sand the car travels in a straight line
STEM
Notes: Think of light passing from air into glass like driving a car from a tarmac road at an angle into sand.
The tyre on the first side to cross onto the sand is slowed down and this turns the car slightly.
Once all four wheels are on the sand, the car continues in a straight line.

## Slide 48: Chromatic aberration through a lens
Light passing through a lens
Different wavelengths (colours) focus at different places
Focusing on one colour leaves others blurred
STEM
Notes: The diagram shows what is happening to the different colours of light passing through a lens.
Different wavelengths (colours) focus at different places. Trying to focus your telescope on one colour leaves others blurred.
https://en.wikipedia.org/wiki/Chromatic_aberration

## Slide 49: Chromatic aberration – correcting
Achromatic doublet
Lens made from two glasses with different refractive indexes
Bi-convex lens – Crown glass
Plano-concave lens – Flint glass
STEM
Notes: One solution to the problem of chromatic aberration is to pair lenses with a different refractive index.
In this example, a bi-convex lens made from crown glass is combined with a plano-concave lens made from flint glass.
The different colours of light now focus very close to the same point.
https://en.wikipedia.org/wiki/Chromatic_aberration

## Slide 50: Light gathering – Diameter and area
Larger opening for light to enter
Swap 50 mm Ø for 100 mm Ø
  50 Ø opening
  mm2
  100 Ø opening
  31,416 mm2
  Doubling the diameter quadruples the area
STEM
Notes: One of the improvements you might consider for your telescope is increasing the amount of light entering your telescope.
Using a larger objective lens will achieve this and the reasons for this are shown by the calculations of diameter and area.
Doubling the diameter increases the area four times!

## Slide 51: Refracting v reflecting telescopes
Refracting – advantages
  Sealed tube excludes dirt
  Sealed tube reduces air movements
  Lighter
  More robust
Refracting – disadvantages
  Eyepiece on the end
  Chromatic aberrations
  Higher cost
Reflecting – advantages
  No chromatic aberration
  Easier to manufacture
  Lower cost for larger scopes
  Larger mirrors are possible
Reflecting – disadvantages
  Open construction allows dirt onto mirrors
  Air movements between the mirrors can cause distortion
  Less robust so more easily damaged
STEM
Notes: This slide lists the main advantages and disadvantages of each type of telescope.

## Slide 52: Newtonian telescope
Most popular design of reflecting telescope
Named after Sir Isaac Newton
  Credited with building the first telescope of this design
  http://www.bbc.co.uk/schools/gcsebitesize/science/edexcel/visiblelight_solarsystem/telescopesrev3.shtml
STEM
Notes: The most popular design of reflecting telescope is called a Newtonian after Sir Isaac Newton who is credited with building the first telescope of this design in 1668.
The light paths for this type of telescope are shown in the cross section diagram.
http://www.bbc.co.uk/schools/gcsebitesize/science/edexcel/visiblelight_solarsystem/telescopesrev3.shtml

## Slide 53: Mirror shaping – small telescopes on earth
Low expansion glass
Cutting, grinding and polishing
Often manufactured by hand
  Videos showing the process
https://www.youtube.com/user/GordonWaite/videos
STEM
Notes: The next few slides describe how mirrors for optical telescopes are manufactured compared with the hexagonal mirrors for the JWST which are designed to capture near infrared wavelengths.
The most critical part of a reflecting telescope is the primary mirror which is parabolic in shape.
Optical telescope mirrors are manufactured by hand from low expansion glass by cutting, grinding, polishing and coating.
Gordon Waite has posted a series of videos on YouTube showing the entire process. The series of videos last several hours so teachers should preview them and pick out key sections to show pupils.
https://www.youtube.com/user/GordonWaite/videos

## Slide 54: Mirror shaping – large telescopes on earth
Single large mirror
Low expansion glass
Honeycomb structure
Computer controlled diamond cutting and polishing
  Video showing the process
https://www.youtube.com/watch?v=MjUcBWYVF9s
STEM
Notes: Traditionally, optical telescopes on earth have a single, very large primary mirror. This video shows one being manufactured at a lab at the University of Arizona. https://www.youtube.com/watch?v=MjUcBWYVF9s

## Slide 55: Mirror shaping – JWST
18 hexagonal mirrors
Made from beryllium
Computer controlled machined
Material removed from the rear of the mirror surface to reduce mass
  Videos showing the process
https://www.youtube.com/watch?v=ZDysmTVoC-k
STEM
Notes: The primary mirror in the JWST is made up of 18 hexagonal mirrors made from a very light but strong metal called Beryllium.
Each hexagonal mirror for the JWST is machined from a solid piece of metal.
The back of the mirrors is machined to form very thin sections and webs to create a rigid but lightweight structure.

## Slide 56: Mirror polishing – JWST
Accurate to within 0.2 x the thickness of a human hair
Computer controlled machines
Very fine abrasive compounds
  Video showing the process
https://www.youtube.com/watch?time_continue=4&v=Y_U_MrWcCnE
STEM
Notes: Polishing of the front surface of the JWST mirrors is done by computer controlled machines and can be seen in the video linked here.
https://www.youtube.com/watch?time_continue=4&v=Y_U_MrWcCnE

## Slide 57: Mirror coating – small telescopes
Reflective coating needed
Aluminium widely used
Applied in a vacuum
Metal is vapourised and settles on the mirror surface
  Video showing the process
https://www.youtube.com/watch?v=MnkmQ_2ri9E
STEM
Notes: Once a mirror is the correct shape, the surface needs to have a reflective coating applied.
The links below explain and demonstrate the process for optical telescopes.
http://www.orionoptics.co.uk/OPTICS/mirrorrecoating.html
https://www.youtube.com/watch?v=MnkmQ_2ri9E

## Slide 58: Mirror coating – JWST
Reflective coating needed
Gold for infrared wavelengths
Applied in a vacuum
Metal is vapourised and settles on the mirror surface
  Video showing the process
https://www.youtube.com/watch?v=fgn7bKs042Q
STEM
Notes: Mirrors on the JWST are coated in gold which is the most suitable material for reflecting infrared radiation.
https://www.youtube.com/watch?v=fgn7bKs042Q

## Slide 59: Eyepieces and pointing systems
Eyepieces with different magnifications changes the field of view
Low magnification for viewing large objects like the Moon
High magnification for viewing small, and distant objects like Saturn
STEM
Notes: Astronomical telescopes have interchangeable eyepieces with different magnifications.
Eyepieces with a lower magnification and wider field of view are suitable for observing large objects like the Moon whilst higher magnification eyepieces will show more detail on small, and distant objects like the rings around Saturn.

## Slide 60: Eyepieces and pointing systems
Start with low magnification
Focus on object of interest
Change to a higher magnification and refocus
Repeat
A small ‘finder scope’ helps with initial alignment
Laser pointers also help with initial alignment
STEM
Notes: Especially at large magnifications, it can be tricky to find objects in the sky.
A small ‘finder scope’ attached to the main telescope has a wider field of view making it easier to point the instruments in the right general direction to begin with.
https://www.telescopeplanet.co.uk/national-geographic-50-600-refractor-telescope
Some astronomers use laser pointers to help orientate their telescopes.
Another technique used by astronomers is to gradually increase the eyepiece magnification, centring and focusing the target in the viewfinder each time before changing to a higher magnification eyepiece.
https://www.tringastro.co.uk/eyepieces--barlows-15-c.asp

## Slide 61: Design improvements
Tube connectors
  Turned (CNC?)
  3D printed
Geared focusing
  Lego or custom designed, computer modelled and laser cut or 3D printed
STEM
Notes: With a better understanding of how telescopes work you may want to improve yours. Here are some ways of improving the performance of telescopes.
Tube connectors
Connectors allow the use of different diameter tubes and can be designed for a smooth sliding motion.
Connectors can also be designed to prevent the tubes coming apart when extended.
Focusing
Sliding the tubes precisely to focus the image can be hit and miss. Using a rack and pinion gear will allow fine adjustment. Construction kits like Lego are a source of precision gears or you can use CAD software to generate gears which could be laser cut or 3D printed.

## Slide 62: Stands and tripods
A sturdy stand is essential
Permanent structures embedded in the ground
Portable stands or tripods
Pan/tilt head is most common
http://www.rocketroberts.com/astro/observatory.htm
STEM
Notes: A sturdy stand is essential when using telescopes especially at high magnification.
Serious astronomers use steel and concrete to create permanent bases for their telescopes.
Folding tripods and portable stands come in many different shapes and sizes and provide plenty of scope for exploring alternative design and methods of manufacture.
http://www.rocketroberts.com/astro/observatory.htm
Pan/tilt movement
This type of mount is ideal when observing things on earth but causes problems when moving the scope by hand when viewing stars.
Panning is a term used in movies and videos and lets you view panoramas and follow things from side to side like birds in flight or vehicles on the move.
To keep stars in view as the earth rotates you have to tilt and pan the telescope at the same time.

## Slide 63: Equatorial mount
Stars move in sky due to Earth rotating
Ascension axis is aligned parallel with the Earth’s axis
  Used to follow the apparent movement of stars
Declination axis perpendicular to the ascension axis
Flexible handles reduce vibration
STEM
Notes: Stars appear to move in the night sky due to the rotation of the earth.
Equatorial mounts were designed with one axis (ascension) parallel to the Earth’s axis. The other axis is at right angles to the Earth’s axis and measures declination.
With this type of mount, you can follow a star by adjusting only the right ascension axis.
https://grabcad.com/library/detailed-planet-earth-model-1
http://www.astronomysource.com/2011/12/17/german-equatorial-mount-part-2/

## Slide 64: Motorised movement
Motorised ascension axis at one revolution in 24 hours makes objects remain still in the viewfinder
Faster speeds to acquire objects initially
Early telescopes used clockwork motors
Modern scopes use geared electric motors
STEM
Notes: If the right ascension axis is motorised at the correct speed, the telescope will keep a star static in the field of view allowing extended observation and time exposure photography.
The rotational speed to achieve this is one revolution in 24 hours.
Early telescopes used a clockwork motor to move the mount. Modern telescopes use electric motors.
http://www.rothervalleyoptics.co.uk/celestron-astromaster-motor-drive-unit.html

## Slide 65: Remote operation
Motorised movement
Digital camera
Viewer can be in a different location
This arrangement uses a Raspberry Pi computer to control the telescope
https://danlr46.wordpress.com/how-to-remotely-control-camera-filter-wheel-and-mount-with-raspberry-pi3/
STEM
Notes: Motorising both axes removes the physical connection between the observer and the telescope completely and any vibrations this might cause.
With remote control of the motors, and a camera or phone capturing the image, you can even observe stars from the comfort of your living room!
The setup on the right uses a Raspberry Pi educational computer to control the movement.

## Slide 66: Remote operation – Large telescopes
National Schools Observatory
Liverpool Telescope
  Located on a small volcanic island
  off the coast of Africa
10% of time allocated to schools in the UK and Ireland
https://www.schoolsobservatory.org/
STEM
Notes: If you fancy serious star gazing using a professional telescope, there are web sites where you can purchase time.
Using a web browser you control the telescope, then capture and download the images that you have taken!
http://www.itelescope.net/
National Schools Observatory
The Liverpool Telescope (LT) was developed by Liverpool John Moores University (LJMU) and 10% of the observing time is allocated to schools in the UK and Ireland.
The National Schools' Observatory (NSO) was created to act as a link between schools and the telescope which is located on a small volcanic island off the coast of Africa.
https://www.schoolsobservatory.org/

## Slide 67: Remote operation – Large telescopes
Faulkes Telescope Project
Free resources for education
Access to a global network of robotic telescopes
http://www.faulkes-telescope.com/
STEM
Notes: This project provides free resources for science education and access to a global network of robotic telescopes.
http://www.faulkes-telescope.com/

## Slide 68: GoTo telescopes
Fully computerised
Database containing the position of thousands of objects
Will ‘find’ a celestial object
Once the domain of professionals and serious amateurs
Prices have dropped significantly
STEM
Notes: Fully computerised telescopes are now available.
They will ‘find’ a chosen star from a database of thousands of celestial objects.
Once the domain of professionals and enthusiasts, GoTo telescopes can now be purchased for less than £300.
https://www.telescopeplanet.co.uk/

## Slide 69: Digital imaging systems
Most digital cameras and smart phones can be used
Adapters link camera and scope
  Scope for custom design and CNC machining or 3D printed
  https://www.thingiverse.com/thing:353135
  https://www.thingiverse.com/thing:2332543
STEM
Notes: With a suitable adapter, almost any camera can be used to capture images from telescopes.
Cameras used for astro-photography range from mobile phones, low cost web cameras, right up to professional single lens reflex (SLR) and mirrorless cameras.
Adapters that hold the camera in the correct position let you concentrate on positioning the telescope and getting the image in focus.
This adapter was custom designed to connect a specific phone and telescope. The shape was designed using parametric CAD software and 3D printed.
With access to 3D CAD software and CNC/3D printing equipment, custom camera/phone adapters can be designed and manufactured.
This phone adapter can be downloaded for 3D printing from Thingiverse, one of several online libraries of 3D models.
https://www.thingiverse.com/thing:353135
Most of the mounts for mid/top range cameras are relatively simple, connecting the lens mount on the camera to the eyepiece tube on the telescope.
https://www.thingiverse.com/thing:2332543

## Slide 70: Early photography
Frenchman Louis Daguerre
First lasting photograph
Silver plated copper sheet
Coated with halogen, iodide, bromine and chorine
Paris boulevard – Louis Daguerre circa 1838/39
https://www.thoughtco.com/an-illustrated-history-of-photography-4122660
STEM
Notes: Frenchman Louis Daguerre is credited with creating the first lasting photograph in 1837.
The image was recorded on a silver plated copper sheet that had been sensitised by coating with gaseous fumes.
A number of chemicals were used including halogen, iodide, bromine and chlorine.
Paris boulevard – Louis Daguerre circa 1838/39
https://www.thoughtco.com/an-illustrated-history-of-photography-4122660

## Slide 71: Developments in photography
Daguerreotype superseded by paper then celluloid film
1900 Eastman Kodak company
Brownie – the first mass produced camera
STEM
Notes: The daguerreotype was superseded by paper and then celluloid with silver bromide coatings.
Both of these can be rolled onto spools which take up very little room in the camera.
In 1900 the Eastman Kodak company introduced the ‘Brownie’, the first mass produced camera.

## Slide 72: First digital camera
Eastman Kodak Company
Steven Sasson – Engineer
1975 – first practical digital camera
Sensor - charged coupled device (CCD)
  https://petapixel.com/2010/08/05/the-worlds-first-digital-camera-by-kodak-and-steve-sasson/
STEM
Notes: In 1975 Steven Sasson, an engineer at Eastman Kodak company, designed and built the first practical digital camera.
It used a charged coupled device (CCD) sensor.
https://petapixel.com/2010/08/05/the-worlds-first-digital-camera-by-kodak-and-steve-sasson/

## Slide 73: How digital cameras work
Make use of article (MUO)
  https://www.makeuseof.com/tag/technology-explained-how-does-a-digital-camera-work/
Wikipedia article
  https://en.wikipedia.org/wiki/Digital_camera#/media/File:Disassembled_digital_camera.jpg
STEM
Notes: The links on this slide explain clearly how digital cameras work.
https://www.makeuseof.com/tag/technology-explained-how-does-a-digital-camera-work/
https://en.wikipedia.org/wiki/Digital_camera#/media/File:Disassembled_digital_camera.jpg

## Slide 74: Digital camera sensors
Charge coupled device (CCD)
  Low power
Complementary metal oxide (CMOS)
Sensors vary in size
Canon APS-H format - One of the largest sensors currently available
  250 megapixels
29.2 mm
20.2 mm
STEM
https://en.wikipedia.org/wiki/Image_sensor_format
Notes: Digital cameras use two main types of sensor; charge coupled (CCD) and complementary metal oxide (CMOS) devices.
The main advantage of CMOS sensors is the low power requirements.
Camera sensors come in many different sizes. https://en.wikipedia.org/wiki/Image_sensor_format

## Slide 75: Filters
IR blocking filter is standard in digital cameras
Limits sensitivity to the visual spectrum
http://dew.globalsystemsscience.org/tools/digital-cameras-overview/
STEM
Notes: Earlier we explained how digital cameras have wide bandwidth sensors with Infra-red blocking filters to allow only visible wavelengths through to the sensor.
The diagram here shows the IR-blocking filter location on top of the sensor inside the camera.
http://dew.globalsystemsscience.org/tools/digital-cameras-overview/
Even with a filter in place, some Infra-red wavelengths reach the sensor and we can see this by viewing a TV remote control through a digital camera.

## Slide 76: Making infrared visible
View a TV remote control through a digital camera
Operate the remote
The infrared LEDs can be seen flashing
STEM
Notes: Point the camera lens at the window at the front of a TV remote control.
Look at the image on the back of the digital camera
At the same time press buttons on the remote. You should see the infra-red LEDs on the front of the remote flashing.

## Slide 77: Converting cameras to infrared
Dis-assemble the camera to reveal the sensor
Remove the IR blocking filter
Re-assemble the camera
Attach an IR pass filter to the front of the lens
  Note Before trying this you MUST get permission from the owner of the camera!
https://www.youtube.com/watch?v=zCJsrh51Ac4
https://www.youtube.com/watch?v=frtQxryDTo8&t=167s
STEM
Notes: This involves the following steps:
Opening the case to reveal the sensor.
Removing the infrared blocking filter.
Re-assembling the camera.
Attaching an infrared pass filter to the front of the lens.
Note: Before trying this you MUST get the permission of the camera owner and your parents.

## Slide 78: Camera modules for programmable systems
IR camera for Raspberry Pi
  NOIR module v2
  8 MP – 640 x 480 pixels
  Fixed focus
IR camera for Arduino
  Linksprite
  IR LED illumination
  Resolution up to 640 x 480 pixels
http://cpc.farnell.com/raspberry-pi/rpi-8mp-noir-camera-board/raspberry-pi-noir-camera-board/dp/SC14029?ICID=I-Rpi-fp2
https://www.open-electronics.org/an-arduino-based-jpeg-camera-with-ir-and-pir/
STEM
Notes: With schools moving to coding lessons, small, single board computers are increasingly being used in classrooms.
Most of these have add-on camera modules that can be converted for infra-red photography.
IR camera module for RasPi
The Raspberry Pi NoIR Camera Module v2 is a high quality 8MP add-on board for Raspberry Pi, featuring a fixed focus lens. The board itself is tiny, at around 25x23x9mm and weighs just over 3g, making it perfect for mobile or other applications where size and weight are important. The camera is perfect for doing IR photography and taking pictures in low light environments.
IR camera module for Arduino
LinkSprite’s serial port camera module can capture high resolution pictures and transport them over TTL serial, making it ideal for embedded applications. And it can do it in the dark, thanks to infrared LEDs.
Resolution - 160 x 120, 320 x 280 and 640 x 480 pixels.

## Slide 79: Telescope body – refracting
Refracting – enclosed tube
  Support lenses
  Excludes stray light and dust
Requirements
  Strong
  Light in weight
  Low thermal expansion
Composite tubes made to order from paper and epoxy resin
http://www.gerdneumann.net/english/instrument-building-parts-teile-fuer-den-fernrohrbau/fernrohrtuben-aus-hartpapier-phenolic-telescope-tubes-hard-paper.html
STEM
Notes: Telescope design has developed over many decades and produced a wide range of shapes, sizes and layouts. The lack of one ‘ideal’ design indicates there is still plenty of room for innovation. Recent developments in materials, CNC machining and 3D printing provide even more opportunities for improving the performance of optical telescopes.
Telescope bodies – Refracting telescope
Most refracting telescopes have a solid tube body. In addition to supporting the lenses in the correct positions, it prevents stray light and dust from entering and reduces air currents.
When choosing material for the tube, look for light weight, low cost and a low thermal expansion.
These composite tubes are made to order for telescopes from paper and epoxy resin.
http://www.gerdneumann.net/english/instrument-building-parts-teile-fuer-den-fernrohrbau/fernrohrtuben-aus-hartpapier-phenolic-telescope-tubes-hard-paper.html

## Slide 80: Telescope body – refracting
Good thermal conductivity
  Acclimatises quickly to ambient temperature
Inside surface painted matt black and ridged to reduce reflections
http://www.protostar.biz/blite.htm
STEM
Notes: Significant distortion can occur if the telescope is at a different temperature to the surroundings so choosing materials with good thermal conductivity for the main structure will help the scope acclimatise more quickly.
The surface inside tubes is usually painted matt black and many scopes have ridges, all designed to cut down internal light reflections.
http://www.protostar.biz/blite.htm

## Slide 81: Telescope body – reflecting
Tubular body is popular for smaller telescopes
Can cause internal air currents
Large tubes slow to reach ambient temperature
http://naturalimagesgallery.com/atm/lh_scope/raw_tube_on_mount.html
STEM
Notes: Reflecting telescope
Some reflecting telescopes use tubular bodies. They are simple to make and support but can cause ‘tube currents’ which distort the image.
Tube currents are caused by the tube warming the cold night air.
Large tubes can take a long time to reach the same temperature as the environment.
Choice of materials plays a large part in the time taken for the temperature to stabilise.
http://naturalimagesgallery.com/atm/lh_scope/raw_tube_on_mount.html

## Slide 82: Telescope body – reflecting
Open tube or truss popular for larger telescopes
Reaches ambient temperature quickly
Lighter than tube bodies
Can be disassembled for transporting
http://www.rothervalleyoptics.co.uk/meade-lightbridge-10-dobsonian-telescope.html
STEM
Notes: Open tube or ‘truss’ designs allow air to flow freely through the instrument shortening the time for the temperature of the telescope to stabilise relative to the environment.
Frame structures also tend to be lighter and can be disassembled to make transporting the telescope to remote dark sky sites easier.
http://www.rothervalleyoptics.co.uk/meade-lightbridge-10-dobsonian-telescope.html

## Slide 83: Telescope design – Image stacking
Several images can be ‘stacked’ to enhance the final image
Telescope must follow the object being photographed
Developed by professional astronomers
Now being used by amateurs
http://www.instructables.com/id/Astrophotography-Star-Photo-Stacking/
STEM
Notes: Digital imaging provided the next significant advance where several images of the same object are ‘stacked’ to create an enhanced image. This has the advantage of cutting down the random coloured dots or ‘noise’ on the image.
Key to this is a telescope that can keep an object in view for an extended period during which several images are recorded.
After the viewing session the images are combined which increases the intensity of the final image.
Professional astronomers first developed this technique which is now commonly used by amateurs.

## Slide 84: Telescope design – Light amplification
Unistellar eVscope
11cm primary mirror
Motorised movement
Database of objects
Images captured electronically
STEM
Notes: Imagine being able to see the result of stacking images in real time.
This is what a start-up company called Unistellar is doing with their innovative eVscope.
Their system is based on a small (11cm diameter mirror) reflecting telescope with motorised axes and a sensitive electronic sensor.
A database containing the position and movement of stellar objects is used to control the motors allowing it to ‘follow’ an object in the sky.

## Slide 85: Telescope design – Light amplification
Images are ‘stacked’ in real time
Electronic viewfinder
The view improves over time as more images of the object are added to the stack
STEM
Notes: Unistellar developed software that captures images and, in real time, combines them into a single image which is projected into the eyepiece.
When a faint object is first acquired, the observer will see very little but, as more and more images are combined, the object will slowly become brighter, sharper and more colourful.
The eVscope is due to go on sale in the summer of 2018.
https://www.kickstarter.com/projects/unistellar/evscope-100-times-more-powerful-than-a-classical-t?ref=blog