## Slide 1: D&T Quick Revision Guide
Mechanisms

## Slide 2: Why learn about mechanisms?
Understanding the uses of and the forces associated with different types of mechanisms is important when developing design ideas and putting them into practice.
Designers use a range of criteria when deciding how mechanisms can work in their designs and the behaviour they require from them if the product is to perform well.
It is important to understand how different mechanisms can be applied to functioning designs and are chosen because of these.

## Slide 3: What is a mechanism?
Mechanisms use movement and forces and transfer them into other movements and forces, in ways that are effective. The most common types of mechanisms are:
Levers
Linkages
Pulleys
Gears
Cams
Different mechanisms can be combined to achieve more complex and efficient outcomes.
Notes: Images: Public domain

## Slide 4: Types of movement
The four main types of movement that are found in mechanisms are:
Rotation
Oscillation
Linear
Reciprocation
Notes: Images: Public domain

## Slide 5: Types of movement 1
Rotation
Turning in a circle, such as in a wheel, wind turbine, cam or gear.
Notes: Images: Public domain

## Slide 6: Types of movement 2
Oscillation
Backwards and forwards motion in an arc, as in a pendulum or swing.
Notes: Images: Public domain

## Slide 7: Types of movement 3
Linear
Movement in straight lines in lever mechanisms and along tracks such as with a train or paper trimmer.
Notes: Images: Public domain

## Slide 8: Types of movement 4
Reciprocation
Repeated back and forth movement as in a sawing action, sewing machine or a piston rod.
Notes: Images: Public domain

## Slide 9: Transfer of movement
Movement can be transferred from rotary to linear, oscillating to linear, etc.
Notes: Images: Public domain

## Slide 10: Transfer of movement 1
Peg and slot
A peg and slot mechanism transfers rotary to oscillating movement.
Beam engines transfer linear energy to rotary through a flywheel.
Notes: Images: Public domain

## Slide 11: Transfer of movement 2
Rack and pinion
A rack and pinion transfers rotary to linear movement.
It can be found in canal lock gates, stair lifts and steering systems.
Notes: Images: Public domain

## Slide 12: Transfer of movement 3
Cams
A cam system transfers rotary to reciprocating movement as in engine exhaust valves.
Notes: Images: Public domain

## Slide 13: Transfer of movement 4
Linkages
Linkages convert linear and rotary movement.
Notes: Images: Public domain; Creative Commons: Simiprof
Examples of linkages’ movements: https://en.wikipedia.org/wiki/Linkage_(mechanical)#Image_gallery

## Slide 14: Organic mechanisms
A range of mechanisms can be found in the natural world, from human and animal limbs (levers) to monkey and mouse tails, fungus spores release mechanisms, the bones of the inner ear and jaw and even gears that help insects to hop.
We have taken inspiration from nature and developed products from adapted natural sources. Velcro was famously adapted from the hooks on burrs.
Artificial limbs mimic and sometimes improve upon the originals.
Notes: Gears in insects: http://www.cam.ac.uk/research/news/functioning-mechanical-gears-seen-in-nature-for-the-first-time
Images: Public domain; Creative Commons: Zina Deretsky, National Science Foundation (after Rita Mehta, UC Davis); Ryan Wilson (pbroks13); University of Cambridge (Profs. Malcolm Burrows & Gregory Sutton)

## Slide 15: Levers
There are three basic types or ‘classes’ of lever:
1 – where the load and the effort lie on opposite sides of the fulcrum.
2 – where the load and the effort are on the same side of the fulcrum.
3 – where the effort the load are both on the same side of the fulcrum, with the effort closer to the fulcrum than the load. This means that more force is put in the effort than is applied to the load.
The position of the fulcrum, the strength of effort and amount of resistance are all variable depending upon what is needed to be done.
Notes: Images: Public domain

## Slide 16: Types of lever 1
Seesaw
The seesaw or crowbar model is where the load (resistance) is on the opposite side of the fulcrum to the force applied (effort).
Notes: Images: Public domain

## Slide 17: Types of lever 2
Wheelbarrow
A wheelbarrow has the load and effort on the same side of the fulcrum.
Notes: Images: Public domain

## Slide 18: Types of lever 3
Tongs
Tongs also have the load and effort on the same side of the fulcrum but greater relative force is needed than in the second example.
Notes: Images: Public domain

## Slide 19: Linkages
Linkages transfer movement direction and type and can change the degree of effort required to move objects. They use fixed and pivoted lengths of material to create movement in different ways, thus enabling rotary to change to oscillating movement, and parallel and reverse direction movements.
Complex systems of linkages can be used with rotary and cam mechanisms to produce creations such as the Strandbeest – a wind powered walking skeleton.
Simpler linkages can be found in pop-up books, deckchairs and adjustable bathroom mirrors.
Notes: Strandbeest: http://www.strandbeest.com/
Images: Public domain

## Slide 20: Types of linkages 1
Treadle action
This converts rotary movement into oscillating e.g. windscreen wipers.
Notes: Images: Public domain

## Slide 21: Types of linkages 2
Fixed pivot
Reverse motion
Pulling or pushing in one direction creates movement in the opposite direction.
Notes: Images: Public domain

## Slide 22: Types of linkages 3
Parallel motion
Moving the bottom bar creates a parallel movement in the top bar.
The pivots and bars can be fixed at different points to create different types of movement.
Fixed pivot
Fixed pivot
Notes: Image: Creative Commons: burts

## Slide 23: Belts and pulleys
A pulley system has two wheels centred on fixed shafts, connected by a flexible belt.
Crossing over the belt will reverse the direction of the wheels, relative to one another.
Chains and sprockets, as on a bike, are other examples of this.
Notes: Images: Public domain
Pulleys: Simple machines video: https://www.youtube.com/watch?v=9T7tGosXM58

## Slide 24: Belts and pulleys
If one wheel is larger the relative turning speeds of the wheels will differ, according to their diameters.
For example, a wheel with a diameter of 30cm will turn at three times the speed of the other with a diameter of 90cm.
DRIVER PULLEY
30 mm
DRIVEN PULLEY
90 mm
Velocity ratio = 90/30
= 3
Notes: Pulleys: Simple machines video: https://www.youtube.com/watch?v=9T7tGosXM58

## Slide 25: Gears
The choice of which gears to use depends on the required outcome.
Worm gears and wheels can be found in guitar machine heads, conveyor belts and gate mechanisms.
Gear trains transmit and reverse drive and increase speed and torque.
Worm
Worm wheel
Notes: Images: Public domain
Gears and wheels video: https://www.youtube.com/watch?v=D_i3PJIYtuY

## Slide 26: Gears
You can use construction kits to explore gear ratios using combinations of two gears:
# teeth | ratio
8, 16 | 2:1
8, 40 | 5:1
8, 24 | 3:1
40, 40 | 1:1
Gear train
Compound gear train
Notes: Images: Public domain

## Slide 27: Cams
Cams convert rotary motion to reciprocating motion.
The cam is a shaped piece that rotates around a shaft. A follower rod follows the profile of the cam and moves up and down in response, guided through a slide.
Cams can be many shapes depending upon the function.
Notes: Images: Public domain
https://msc-ks3technology.wikispaces.com/Cams

## Slide 28: Cams
Pear or egg cam
Examples include engine exhaust valves, locks, clocks and mechanical toys.
Notes: Images: Creative Commons: ThyssenKrupp Presta Chemnitz GmbH; IJB TA

## Slide 29: Cams
Eccentric cam
Examples include steam train wheels and mechanical toys.
Notes: Images: Public domain

## Slide 30: Cams
Drop cam
Examples include clock mechanisms and toys.
The mechanism, which works in a similar way to a pendulum driven ratchet wheel, can only really rotate in one direction or the cam and follower will jam.
Notes: Images: Public domain

## Slide 31: Springs and screws
Coiled springs can resist being compressed, as in a mattress, or use tension, where the spring resists stretching, for example to keep a valve closed.
Hair springs are fine coiled springs used in clocks, causing a balance wheel to oscillate.
Notes: Images: Public domain; Creative Commons: Siberwolf

## Slide 32: Springs and screws
Leaf springs are typically used in vehicle suspension.
A bow is a type of spring, holding tension until the arrow is released.
Notes: Images: Public domain

## Slide 33: Springs and screws
Screws
The helix in a screw can be used to move plates, as in a vice; raise and lower a weight, as in a car jack, or raise water from a well using an Archimedes screw.
Notes: Images: Public domain; Creative Commons: Siberwolf

## Slide 34: Hydraulic systems
These use liquids to transfer energy along pipes and deliver an output.
Liquids do not compress so transfer energy in proportion to the input, while gasses will compress and absorb some of the input energy.
Examples of hydraulic systems include car braking and suspension systems, mechanical diggers, and tipper trucks.
Notes: Image: Public domain

## Slide 35: Pneumatic systems
Pneumatic systems use gasses to transfer energy along pipes and deliver an output. The resulting output can be regulated, for example to power an industrial digger, or can use sudden release for launching an air powered vehicle or a nail gun.
Gasses will compress and absorb some of the input energy while liquids do not compress so transfer energy in proportion to the input.
Pneumatic systems include power tools such as a road drill and in machine tools and robotics.
Notes: Image: Public domain

## Slide 36: Forces
Mechanisms use and resist forces to make them work efficiently. Forces include gravity and friction.
Input – movement of a mechanical or pneumatic type that initiates a response movement in the mechanism.
Output – the result of processing input movement as, for example, rotation or linear actions.
Compression – the effect of forces pushing on and trying to squeeze (compress) an object, for example in a pneumatic system or a spring.
Tension – forces that try to pull apart an object, as in a spring in weighing scales.
Links to Science
Notes: Images: Public domain

## Slide 37: Some ideas
You might use mechanisms in designing and making the following products:
Automata such as animated film props would combine pneumatics with levers and linkages.
Lifting heavy weights can be done using pulleys.
A display in a shop window might use cams, levers and linkages and pneumatics.
Jack-in-the-Box toy or a board game with mechanical parts.
Disassembly – take apart a bike brake mechanism to see how the parts work together.
Any ideas might make use of systems and control technology, including programming and control.
Notes: Images: Public domain

## Slide 38: Activities
Categorisation: Which mechanisms would you find in the following (some may include more than one)?
 | Levers | Linkages | Pulleys | Gears | Cams | Springs | Pneumatic
Remote control toy spider |  |  |  |  |  |  | 
Bicycle |  |  |  |  |  |  | 
Security doors |  |  |  |  |  |  | 
Crane |  |  |  |  |  |  | 
Fairground ride |  |  |  |  |  |  | 
Industrial robot welder |  |  |  |  |  |  | 
Aeroplane wheel system |  |  |  |  |  |  | 
Washing machine |  |  |  |  |  |  | 

## Slide 39: Activities
Spider legs
Using construction kit materials or card and fasteners make a prototype of a walking robot insect leg.
You might connect this to a motor to power the action.
How might you improve upon your design?
What would be the effect of moving the joints or changing the length of the rods?
Notes: Robotics Mechatronics resource: https://www.data.org.uk/shop-products/robotics-mechatronics/
Image: Public domain

## Slide 40: Activities
Lift off
Can you devise a mechanism to raise a heavy weight without touching it?
You might use levers, linkages, gears, pulleys and/or pneumatics.
Draw your design labelling the parts and forces involved.
Think about other factors such as stabilising the load, keeping it safe for workers to operate and accurate positioning.
Notes: Image: Public domain

## Slide 41: Activities
Turning around
Think about:
Who might need a device that uses a powered gear mechanism?
What product can you develop using an electric circuit and gears to meet their needs?
How fast should it rotate and how can you change the speed of rotation?
Explore combinations of two different size gears meshed together using a construction kit. Investigate the direction and speed of rotation noting how the size of the driver gear affects the speed of the follower gear. Use the number of teeth on each gear to decide the gear ratios.
Build a model using a working circuit with a battery, motor and switch, such as a reversing switch. Draw a circuit diagram using correct symbols.
Notes: Image: Public domain