## Slide 1: KS3 d&T contexts Minimising parts
#InspiredbyKI
Notes: Please note; This resource, accompanying resources and associated images, videos and graphics are to be used for educational purposes only and in line with our terms and conditions as stated here. https://www.designtechnology.org.uk/terms-and-conditions-and-policies/

## Slide 2: About this resource
Overview
KI is an innovator in the contract furnishing industry with offices across the UK and Europe. This context asks you to consider ‘minimising parts’.
Area(s) of focus
Furniture design, ergonomics, manufacturing.
Links to the National Curriculum
The resource covers a full design, make and evaluate process, but also suggests investigative and evaluative activities, and relevant focused tasks.
Technical knowledge: CAD, CAM, modelling, ergonomics, rapid prototyping, manufacturing processes, maths and science, visual and technical communication.
Included in this resource are a range of images, photographs and videos. Some of the materials in this resource have been created by KI Europe- the D&T Association hereby acknowledges and thanks KI Europe for its contribution. Without this, it would not have been possible to produce this, which is freely available to all teachers.
Notes: General information about the resource to help you decide if it is right for your needs.

## Slide 3
Suggested level: Mid/late key stage 3*
Duration: Approx. 10-12 weeks
Focus: Innovation, UCD, ergonomics, anthropometrics, sustainability, innovation
Materials: Multi-materials
Processes: Designing, shaping and forming, manufacturing, science, engineering
Systems: Mechanical, structural, CAD, CAM
Responsibilities: Health and safety, sustainability, ethics, six R’s
*you can use the resource at whichever level you feel it is appropriate.
Notes: A summary of the resource so you can check it meets your curriculum requirements

## Slide 4: Contents
Design Context
Empathize
Define
Ideate
Prototype
Test
Focused Tasks
Investigative and Evaluative Activities
Supporting units
Notes: Click the headings to get further information. Feel free to delete / edit the table to provide more or less for your students.

## Slide 5
Notes: Introductory video

## Slide 6: Introduction
KI is a manufacturer of contract furniture (designed and made for public environments) with offices across the UK and Europe. Their focus is not just designing quality furniture, but also crafting high performance environments while remaining committed to the goals of innovation, sustainability and timeless design.
The context for this unit is:
Minimising parts
The following slides show how the design team at KI would approach this context in relation to the five main stage of the design process: empathize, define, ideate, prototype, test. You can follow a similar process to create your solution to creating great furniture designs while minimising parts!
Notes: Introduction to the context

## Slide 7
Notes: Empathize video

## Slide 8: Empathize stage
Your first task is to put yourself into the shoes of the potential user of the furniture you are designing. At this stage you are simply trying to understand what some of the problems may be. The more the merrier! There are no wrong ideas/thoughts at this stage! There are many ways that KI, and other companies do this. Consider trying some of these methods:
‘What does a customer want?’ | ‘Environment’ | ‘Get involved’
Understanding the needs of the customer is vital to designing a product that will be useful for the target market. Try and observe people using furniture in a variety of situations and not always how you expect. How do they open a cupboard door while holding a drink, or move a piece of furniture around on wheels when carrying something? | While sustainability is a key focus of the work at KI, it is important to consider the environments (places) where the furniture will be used. While it may be possible to make a list of standard feature in offices etc. consider more diverse environments where usage and access may be very different. | Empathetic design extends to experiencing what the user will when using furniture. Try assembling furniture from flat-pack or using it day to day to see if there are any challenges or difficulties you could address in your approach to designing a new piece of furniture.
Notes: Click the headings to get further information. Feel free to delete / edit the table to provide more or less for your students.

## Slide 9: Break down the context
The context is deliberately simple so you can investigate and determine your own approach to exploring design opportunities. This contexts encourage an empathetic approach to analysing and investigating the design situation.
WHERE?
DESIGN PROBLEM
WHY?
WHAT?
WHEN?
HOW?
WHO?
LOCATION
HOME
OFFICE
FUNCTION
PURPOSE
MATERIALS
USER
NEEDS
DAYTIME
HOLIDAYS
Notes: A mind map approach to breaking down the context. Edit to suit.

## Slide 10
Notes: Defining the nature of the product

## Slide 11: Define stage
You now need to define your focus. This means you need to state what it is you are trying to do. You need to be precise and clearly state your brief. Who is it for, what will it do, why is it important? To help you with the define stage, use one or more of these:
‘USP’ | ‘Fashion’ | ‘What to minimise parts of?’
For a product to be successful, it needs to have a ‘unique selling point’ (USP). Look at the existing products on the market and ask how you could make your design better, more cost efficient, sustainable or interesting. This could be a feature that makes it easier to manufacture, arrange or dispose of. Alternatively, it could be its appearance or functionality that makes it stand out. | Fashions and trends define the way we dress and the décor in the environments where we live and work. Try and identify current trends in interiors and architecture. Do they use particular shapes, materials, colours etc. Can you use inspiration from design periods in history to ‘invent’ your own trend based on what elements are popular at the moment? | Consider what aspects of furniture you can reduce or minimise. Will this make it lighter, more cost effective, easier to manufacture or recycle? It might be that you want to standardise the fittings to make it easier to assemble with minimal tools. You might wish to consider if parts of the furniture can serve more than one function, so you don’t need so many different parts.
Notes: Click the headings to get further information. Feel free to delete / edit the table to provide more or less for your students.

## Slide 12: Define stage
Consider these aspects when defining and designing your product.
Function
Purpose
User
Authenticity
Innovation
What it is intended to do
Who it’s intended for
How it works
Is it relevant, realistic and feasible?
What unique features it has
Notes: Five key criteria to consider when designing

## Slide 13: Define stage
The context ‘minimising parts’ provides an overview of the design opportunity, but it may be useful to encourage students to create their own more focused design briefs, so they have some criteria to refer back to when investigating the context and developing their own solutions. It could be as simple as:
“Design easy-to-assemble seating for a school nursery”
A simple statement of the design problem to be solved 
Notes: Suggesting a brief for the context

## Slide 14: Specification
A Product Design Specification (PDS) provides more detailed criteria for the intended outcomes to ensure it meets the needs of the customer or the market.
While the design brief is a starting point, the PDS can be very specific in terms of size, materials, production, packaging, cost etc. The production of a detailed PDS is a requirement at GCSE so it is a good idea to incorporate them into your KS3 design work.
A common list of criteria might include: aesthetics, cost, dimensions, function, human factors, social, moral and environmental concerns, manufacture, materials, safety, target market etc.
Notes: Do students need to write a specification for this context?

## Slide 15
Notes: The ideation stage explained by a member of the design team

## Slide 16: Ideate stage
You are trying to consider lots of different ideas for your solution to this context, so you have lots of design choices. It is also a chance to eliminate as many potential problems as possible.
These don’t need to be detailed and accurate at this stage. Try some of the approaches the designers recommend:
‘Profile sketches’ | ‘Parametric models’ | ‘View it in different ways’
A lot of furniture can be defined by its ‘profile’ such as a table or chair. If you draw it from the side, you can understand the general shape of the product without needing further views. At the early stage of designing, these quick profile sketches can be used to show scale, form and assembly ideas without spending too long on 3D sketches which may not be necessary. | Using parametric CAD software to make models allows for changes to be made to the model quite easily with the results shown on screen instantly. This is useful of you want to change the angle of a leg, or the height of the back without drawing a new design or making a card or foam model. Using this approach, many different iterations of a design can be created in a short space of time and tested on screen or through 3D printed or laser cut outcomes. | We often use SCAMPER when developing ideas which suggest ways of changing the design. This might involve flipping it over, removing or substituting a component, or combining different elements. Try to think differently from what is ‘normal’ or expected and you might just come up with a really unique design!
Notes: Click the headings to get further information. Feel free to delete / edit the table to provide more or less for your students.

## Slide 17: Ideate stage
Ideation is the process of realising our ideas then developing them towards a prototype. Try some of these in this context:
Quick sketches: spend 5-10 minutes per sketch to avoid design fixation.
CAD ‘sketch models’: use a simple CAD package to generate quick and simple ideas.
With both of these methods it’s time to throw caution to the wind and just get some quick ideas down.
Getting stuck for ideas?
Try the SCAMPER approach to generating new ideas.
Think differently, ask yourself why furniture looks or works a certain way. Is it just because it’s always been like that, and does it need to stay the same?
Notes: Some suggestions of how to ideate and develop ideas

## Slide 18: Ideate stage
Different approaches to the design can be taken, but setting limits or restrictions can actually help to drive creative solutions.
Can you redesign an existing solution to use less parts?
What ideas can you create that are made from a single part?
How can your design be modular, so the customer only buys the parts they need?
Could you make it multifunctional so that additional pieces are needed to provide more than one purpose?
Can you reduce materials in your designs?
Can you design furniture that could be repurposed for different applications?
Can you standardise the fittings or reduce the need for tools?
Notes: Some considerations for how to generate ideas for the design

## Slide 19: Ideate stage
You have access to two basic starting points of tables that require no / limited fixings. Laser cut these from 3mm manufactured board and assemble them. Consider how these can be improved to make them a worthwhile piece of furniture.
Notes: Files are downloaded with this context and are available in .dxf and Techsoft formats. Students can use these to develop / improve connection methods, shapes, stability and more. This may be done using card / scissors, or editing using a computer and iterating on a laser cutter.

## Slide 20
Notes: Prototype video

## Slide 21: Prototype stage
At some point you will need to prototype your idea. This is to see if what you are trying to do, will work or not. Your prototype may incorporate some sort of mechanical operation. How will people operate it? Will it be fixed onto something else or be place on the floor? What do you need to prototype to test it out?
‘Prototype in CAD’ | ‘3D printing’ | ‘Remote manufacturing’
Today’s CAD software is so advanced that you can create an accurate 3D model on screen that looks and behave like the real thing. This includes the material properties, how parts assemble/fit together and even how it will perform in use. With the ability to place it in an environment and render a photo-realistic image, there is less need to make a physical prototype when developing the design. | The low cost of rapid prototyping technology such as 3D printing means schools can now have access to rapid prototyping technologies allowing you to hold a physical version of your CAD model in a relatively short space of time. You may not be able to print a full-size piece of furniture, but you can make a scale model or even full-size components to test! | Few companies make the products they design and develop. They send them out to manufacturing companies who will often want the 3D CAD data in model or drawing form in order to manufacture them. Understanding this process is a good way to reinforce the need for accurate modelling of objects and components. Try doing this with your designs and see if another student could proceed with manufacturing with the information you give them!
Notes: Click the headings to get further information. Feel free to delete / edit the table to provide more or less for your students.

## Slide 22: Prototype stage
This context lends itself well to both physical and CAD modelling as a means of developing a working prototype.
Polymorph, plasticine, and foam are all great materials for realising organic or curved forms effectively. Card can be used for more box-like shapes.
You could also use laser cutting or 3D printing in the development and prototyping stages so quick results can be achieved.
The final prototype could be created with greater accuracy by making use of CNC machinery.
For making skills that this resource could address, refer to the curriculum units relevant to the materials or processes you wish to cover in your teaching.
Notes: This context can make use of CAD and physical modelling

## Slide 23: Prototype stage
CAD can be used to create a 3D model which can be viewed on screen but also 3D printed at scale to see how it will look. It can also be tested with a mannequin or other scale figure.
We can also use FEA (Finite Element Analysis) to test how the structure will perform before we make a model or prototype of it. See the supporting unit linked to this context for more details.
Notes: An example of FEA using Solidedge

## Slide 24
Notes: Test stage video

## Slide 25: Test stage
‘CAD testing’ | ‘Testing all parts’
The manufacture of products is a very expensive process, so we don’t want the products to fail. Virtual testing is now built-in to most CAD packages and lets you evaluate the look and form of a product, but also how it performs in use and under load or stress. This is called Finite Element Analysis (FEA). Look for this feature in your CAD software and try it out on your designs. Remember that you can still make a prototype to test yourself, but this process could save you a lot of time making an outcome that might not work! | It is important to consider the life cycle of a product from obtaining materials, to manufacture, use, and eventual disposal. Concentrate on the use of the product and how it is assembled. Is it easy to build or adjust? Does it work as intended? Can it operate under more extreme conditions of moisture, heat, weight, abrasion etc. Don’t restrict testing to how you think it will be used and be sure to test all components or elements, not just one part!
The iterative design process will require the outcomes to be tested against the original intentions so you can see how well your design would meet the needs of the user. This could involve testing the outcome yourself or giving the prototype to others to use and evaluate. The following are methods discussed in the video:
Notes: Click the headings to get further information. Feel free to delete / edit the table to provide more or less for your students.

## Slide 26: Image bank
Notes: The following images may be useful to share with students and/or to use to create additional resources for your work in this unit.

## Slide 27: Image bank
Notes: The following images may be useful to share with students and/or to use to create additional resources for your work in this unit.

## Slide 28: Focused Tasks
During the exploration and development of ‘minimising parts’, there are a number of focused tasks you could use in this unit of work to support the design process or simply use the context as a vehicle to deliver these particular skills. The following are just some it lends itself well to:
‘CAD modelling’ | ‘3D printing’ | ‘Stackable stools’ | ‘In-situ’
Use CAD to create early idea concepts as well as more detailed components for working assemblies and for rapid prototyping. Encourage the idea of ‘sketch modelling’ using CAD. | Investigate how CAD models can be converted for 3D printing. Get students to understand the different orientation, speed of print, and other settings can affect the quality of outcome. | Students are to design a small (scale), stacking stool that can be used in school or offices. These should then be printed out and tested to see if they are able to stack safely, and easy to remove. | Using a program such as Sketchup, design a room plan for a client of your choice. This may be an IT firm, a playcentre, restaurant, or something completely different. It helps for clients to see their furniture where it’s intended, or ‘in-situ’.
‘Laminating’ |  | ‘Physical testing’ | 
Laminating wood has been used since the 1800’s, but became popular for furniture in the 1930’s. Using card or wooden veneers, create some simple, curved shapes by gluing strips in a former. |  | Provide students with a 3D CAD design that they can edit to make lighter / smaller and still withstand set structural requirements. Test with weights and see the points that it bends / deforms. Plot the results in a graph. | 
Notes: Click the titles to access member Focused Tasks and Investigative & Evaluative Activities in detail.

## Slide 29: Investigative & Evaluative Activities
The investigate, or research, element of this project should be relatively easy to carry out as furniture and furnishings are all around us. However, consider looking at a wide range of furniture in a wide range of different environments. See if you can spot opportunities for minimising parts in the construction or use of your designs. Think about how you can create something unique from what you discover in your research.
‘Evolution of the chair’ | ‘CAD testing’ | ‘Making materials’ | ‘Sustainable redesign’
Furniture and furnishings, like clothing, are subject to fashion and trends. Since the first records of furniture being used, chairs have evolved to take advantage of new materials and technologies as well as fashion. Investigate the history of the chair and how it evolved through the 20th Century. Where are we now in terms of design trends and technologies? | FEA (Finite Element Analysis) is a form of virtual stress testing built into many CAD packages. Using the 3D CAD model from the focused tasks, use the FEA in your CAD package to test the model by applying forces to it. | Furniture can be made from a variety of materials, but why are certain materials used? Experiment with making your own materials such as paper pulp for casting, recycled plastic bottle tops or recycled filament for 3D printers. There are some interesting case studies online such as: https://www.kieurope.com/about-us/blog/the-next-evolution-of-sustainable-seating-postura-wood-mix-finish/ | Provide a design for a piece of furniture, how can this be made more sustainable? Are students able to remove unnecessary parts, use alternative materials? They should present their design and benefits (such as costings) to an audience.
Notes: Click the titles to access member Focused Tasks and Investigative & Evaluative Activities in detail.

## Slide 30: Empathize tasks
‘What does a customer want?’ | ‘Environment’
Consider holistic design where you consider all aspects of the problem. This will often require focusing on the bigger picture, not just the design itself. Ask what, why, who, where questions form a picture of the individual’s needs. Consider as many users as you can (Who). What are their particular needs. Remember also that design such be sustainable and inclusive so should focus on being accessible for all users. What furniture is already available and what is its main function? You may want to focus on one environment or activity and look at it like a ripple diagram (below), each ripple being a different category – who, where, what, why, when etc. This may help spark further areas to consider: | No product exists in isolation. Consider the different environments where we use furniture. Make a list of all features that may be useful e.g. the flooring type, if it’s a bright / dull room, where plug sockets are etc. Students should explain why they feel it is important (e.g. carpet – so castors won’t work well, things may mark the carpet…) Consider the mood of rooms also e.g. Home - think of where you sleep, study, rest, eat etc. How is the furniture different, does it match the environment? Work – this could be a place of work, your school or a college//university. How is the furniture there different from home? Rest and play – when you are relaxing do you need a different type of furniture? What about hobbies and pastimes, gaming and use of social media. Is the function different or how you interact with it? Does your posture change when doing this sort of activity? Well-being – how is the furniture different in a gym, spa or hotel. How is the furniture in a hospital or clinic? Are a lot of people using it for different purposes? Does it need to be more durable, adaptable etc? Get photos of the area you are focusing on, measure it and annotate with dimensions and observations.
Student
Home
School
Restaurant
Office
Lounge
Watching
TV
Studying
Gaming
Working
Chilling
Difficulty
interacting
Frustrating
to use
Need tools
Limited functions
Not big enough
Customisable
Expandable
Eating
Too complicated
Portable
Multi- function
Reduce weight
Modular
Sleeping
Not on trend
Sustainable
Repurposed
Notes: Feel free to edit / use these with your class as appropriate. Change the wording and share with students if you wish, or use to help your own planning.

## Slide 31: Empathize tasks
‘Get involved’
Try to get hold of some flat-pack furniture that you can make in a group. You may be able to find these second-hand on a local online marketplace, or within the school community. Most of the time you will be able to disassemble them (if they haven’t been glued). The process of disassembling and assembling furniture can help students highlight issues. What do they find hard? For example, some companies discovered people struggling to put in panel pins to the back of their cabinets to hold the hardboard sheet in place, putting them in inaccurately and so splitting the wood. As a result, many now include a pin guide to hold the panel pin and keep it a set distance from the edge. Students can list the things they found hard, but also bits that were helpful in the process (i.e. numbering bags, only requiring one tool).
Notes: Feel free to edit / use these with your class as appropriate. Change the wording and share with students if you wish, or use to help your own planning.

## Slide 32: Define tasks
‘USP’
There are so many products on the market nowadays. What makes one stand out from another? Look at existing products that are instantly recognisable and ‘desirable’. Ask your students to name the product that comes to mind for these categories: Smartphones Tablets Cars Gaming consoles Toys Trainers What is their USP? Discuss what makes that product unique or stand out in the market? Relate this to the context. What item of furniture from experience or their research stood out as being different or ‘unique’? What was its USP? Make a list of these USP features and use them to define the criteria the student will want to try and incorporate in their designs. Consider marketing early on What will you use in your marketing? Consider showing iphone adverts through the years (copied on the right) where they alter the main selling point of the phone. In recent years, the benefit of the camera seems to be the main element they are focussing on. What will be the students’ ‘best in class’ part about their furniture?
Notes: Feel free to edit / use these with your class as appropriate. Change the wording and share with students if you wish, or use to help your own planning.

## Slide 33: Define tasks
‘Fashion’ | ‘What to minimise parts of?’
Produce an annotated moodboard using magazines, the internet, fabric samples and other sources if appropriate. They should focus on things other than furniture, for example, maybe concentrate on sportswear trends – look at any materials, shapes, patterns and textures that companies are using in football boots. Consider architecture, packaging, vehicles… are there bits that students can pull out to influence their design. Try to aim for keywords that summarise current looks. | The context is focused on minimising parts which links naturally to sustainability but remember to focus on how and why we are minimising part while still maintaining things like functionality, ergonomics and aesthetics. Here are a few things to consider ‘minimising’: Aesthetics - does it look considerably smaller, thinner or lighter. Consider the Apple iPad and how they are always trying to reduce its thickness or weight. Cost – is the reduction in materials or components saving on production costs and being passed on to the customer? Dimensions- are we noticeably reducing size and/or weight? Durability – is minimising parts affecting its durability? Function- can it still function as intended with less parts? Sustainability – are we making a more sustainable product that is less harmful to the environment in terms of material extraction and processing? Manufacture – is this new design easier to manufacture? Safety – is it still safe to use? Life cycle– Have we made it easier to add to, adapt or repurpose so it doesn’t need to be replaced as often (or at all)?
Notes: Feel free to edit / use these with your class as appropriate. Change the wording and share with students if you wish, or use to help your own planning.

## Slide 34: Define tasks
What do we mean by ‘minimising parts’ and what is the benefit?
This could mean minimising the number of elements or components in a piece of furniture.
It could be about reducing the material needed.
Consider all the different things that could be minimised with a piece of furniture and consider the benefits and possible problems with it.
Notes: An example of a simple task to aid discussion about what we mean by ‘minimising parts’.

## Slide 35: Define tasks
Consider all the different things that could be minimised with a piece of furniture and consider the benefits and possible problems with it.
What to minimise? | Why? | Who wins? | Who loses?
Number of components (e.g. mechanical fixings) | To save cost, save time to make, may be simpler | User = cheaper to buy Manufacturer = less parts to organise | Company that supplies them. May not be cheaper as it will need redesigning
Weight | Save on fuel, easier to move around | Less fuel for lorries, cheaper material, better for the planet | May not be as sturdy? Feels cheap?
No padded seat | Could create a moulded texture to prevent slipping, more ergonomic shape | Easier to clean / maintain | ?
Size | Smaller living spaces | ? | ?
? | ? | ? | ?
Notes: Consider getting students to do this on a piece of paper or digitally. Deciding on the group, you may want to provide some prompts as a back-up. Consider allowing them to choose how to present the data, it may be an opportunity to discuss methods of communication.

## Slide 36: Define tasks
Spot the difference!
The ‘Kallax’ is nearly identical to the ‘Expedit’, with the same internal sizes and fittings. The major difference is the thickness of the wood that makes the outer edge is slimmed down.
Images © IKEA
Notes: Ikea uses one percent of the world’s wood supply. When selling tens of millions of bookcases a year, the small saving per bookcase can really add up. The change in design saves Ikea money when it comes to manufacturing and helps the company create more sustainable products that are better for the planet.

## Slide 37: Define tasks
Using the cards available, rank the chairs from Best to Worst
Some prompts may change your mind...
Best for the environment
Transporting
Recycling
How it’s manufactured
Overall
Notes: An opportunity to work in groups to discuss the environmental impact of chairs, considering elements of a product life cycle. Some are stackable, some have mixed materials, some can be repaired/parts replaced… There’s also opportunities to discuss fashion/colourways, properties of materials with regards to fabrics, woods, polymers…
Cards are available to print off and cut out on the next slide.

## Slide 38
Notes: To print and cut out as cards for discussion

## Slide 39: Ideate tasks
‘Profile sketches’ | ‘Parametric models’
Many items of furniture are recognisable by their profile. Think of orthographic views where you are looking at the front, side etc. Your students can save time drawing in 3D in the early stages of ideation by just sketching out the profiles. These could be used to: Scale and proportion. Drawing just the profile we can get a feel for the thickness of materials, the proportion etc. It’s also much easier to change or redraw a profile sketch. Ergonomics. Using readily available ergonomes that can be printed off. You could use these to sketch the profiles to match the scale and proportion of the human form (see next slide). Assembly and fittings. It is easier to show where parts fit together or how they move or operate from a ‘flat’ profile view Interaction with other furniture. Student will often draw one element of a set of furniture, such as a chair, without considering how it interacts with a desk or how a wheelchair might need to access furniture. Trying to draw all these elements in 3D can get very complicated so stick to simple profile sketches. Aesthetics. You can tell a lot from the profile of a piece of furniture in terms of form, proportion, curvature etc. These can help to define the object in the early stage of ideation so they can be developed further as it develops. As ideas progress, the drawing / render / sketch will likely increase in complexity, but keeping the initial ideas simpler will help to develop the important fundamental aspects of the design. | Not all software is parametric. Can your students define/understand what parametric modelling is and use the most suitable software when developing their designs? SketchUp and Tinkercad. Often used by younger learners due to the simple interface and access to modelling tools. Neither is parametric, there is no feature or history tree that can be edited. While you can edit dimensions at any time in Tinkercad making it more useful, SketchUp is difficult to work with when you want to change dimensions later. Onshape. One of the best packages to use as its cloud based and intuitive to use. It has a full set of parametric modelling tools and is very accurate. Fusion and Solidedge. These are industry standard packages that have all the main features you would need but also the ability to render out images. Solidedge has generative design included as standard Solidworks. Has all the features of the software listed above, but is not free. It is. however, the most widely used software in industry so well worth learning and using if you have it. Choose from the software above based on your needs and resources and follow the tutorials in the curriculum units to use parametric modelling in your D&T lessons.
Notes: Feel free to edit / use these with your class as appropriate. Change the wording and share with students if you wish, or use to help your own planning.

## Slide 40: Ideate tasks
‘View it in different ways’
The 800 series is one example of where things were viewed in a different way to come up with an alternative solution. One famous example is the designer of the mini, Alec Issigonis. Issigonis took a car engine and turned it 90 degrees, creating what is known as a transverse engine which left a lot more space in the car. He also put the gearbox in the bottom of the engine, saving yet more space. By asking the question “Why not turn the engine around and put the gearbox underneath?” he managed to create a revolutionary design. Try getting students to design a table and they are likely to draw a rectangle with 4 legs. Get them to consider what a table must do, and design for that, and it may alter. For example, it may be initially as simple as ‘hold something up off the floor’. Outcomes may be chains from the ceiling, a central pillar, a series of upright dowels… This alternative starting point may prove useful in creating original designs. You may also want to share famous furniture designs for discussion.
The wiggle chair: Frank Gehry
Up armchair: Gaetano Pesce
Nooguchi coffee table: Isamu Noguchi
Notes: Feel free to edit / use these with your class as appropriate. Change the wording and share with students if you wish, or use to help your own planning.

## Slide 41: Ideate tasks
S
C
A
M
P
E
R
SUBSTITUTE
COMBINE
ADAPT
MODIFY
PUT TO OTHER USE
ELIMINATE
REARRANGE
Can I substitute materials, change one part for another, change feelings or attitudes towards it?
Can I combine materials or parts? Can I combine things to give it more uses?
What part can I change? What can I borrow from other people’s designs? Can I adapt a different process?
What can I make bigger/smaller? Can I exaggerate bits? Can I increase manufacture speed? Add extra value?
What else can it be used for? Can different people use it? Are there new ways to use it?
Can I remove parts without affecting the function? Can I simplify it? Can I cut costs?
Can I change the way it’s assembled? Can I swap components, the pattern or layout?
Notes: Feel free to edit / use these with your class as appropriate. Change the wording and share with students if you wish, or use to help your own planning.

## Slide 42: Ideate tasks
Introduce dairy alternatives such as almond and oat milk
Repurpose it’s space to allow people to work from there.
Stop using plastic straws in favour of sustainable alternatives.
Combine loyalty programs and mobile ordering to give rewards.
Implement mobile ordering and payment methods
Phase out less popular items.
Introduce self-service points.
Modify their Happy Meals to include healthy options.
Introduce sustainable materials to substitute synthetic materials.
Modify their shoes to incorporate technology, adding to comfort.
Add manufacturing waste into the production of new products..
Branch out into fashion, from purely athletics / sports.
Take a look at some of the following case studies of companies who have used some of the ‘SCAMPER’ elements.
Notes: Feel free to edit / use these with your class as appropriate. Change the wording and share with students if you wish, or use to help your own planning.

## Slide 43: Ideate stage
KI have a range of chairs that use the same back, but with alternative legs. As part of this context you have access to a 3D-printable file whereby you can experiment with your own leg designs. This may be using soldering/brazing, casting using kinetic sand, bent wire or more. These can be tested in terms of stability and style.
Notes: Case study

## Slide 44: Ideate tasks
Profile sketches can be useful to get an idea of shape and proportion. When used with an ergonome, you can also see how a person may interact with it and provide an idea of scale too.
Notes: Feel free to edit / use these with your class as appropriate. Change the wording and share with students if you wish, or use to help your own planning.

## Slide 45: Ideate tasks
Print this ergonome onto card, cut out then assemble using paper fasteners.
Notes: Feel free to edit / use these with your class as appropriate. Change the wording and share with students if you wish, or use to help your own planning.

## Slide 46: Prototype tasks
‘Prototype in CAD’ | ‘3D printing’
We have already covered the advances in CAD software and the features available in most software now available free for teacher and student use. While a physical outcome will always be useful for testing and evaluating before putting it into mass production, you can now prototype an idea in CAD almost to the point of production. Try the following to create an accurate prototype in CAD: Make all parts/components accurately as you would if they were being manufacture and ensure they are accurately dimensioned and to the right scale. Assemble all the parts using the CAD software’s mating tools. This will ensure they connects and interact exactly as intended. This includes mechanical mates so that sliders, gears, levers etc. operate as they would in the real world. Assign the correct materials to the parts so they can be tested. Apply the right visual materials or textures for rendering. Add the little details such as cups, lights, cushions to make it look more realistic Place it in a virtual environment on screen, or using AR. Render out your images along with evidence of FEA and any animations you may have created. These will all support and validate your ideas. | Consider the purpose of creating a prototype. Is it to check the aesthetics, scale, proportion etc. or is it to test functionality and how it can actually be used by a person? 3D printing will likely be limited to a scale model, but this can be useful to interact with a physical. You can still do various test on there to see how it would function or perform under load. A visual prototype such as this may be more concerned with aesthetics; how it looks, feels, sounds. You could also use 3D printing to create full size components such as handles, connectors etc. There could be used in a test rig to see how they would function in a full-size prototype and, when combined with a scale model, could be useful. These ‘proof of concepts can be a model or more detailed prototype that is made to prove the idea or principle works. They can also be used to explore remote manufacturing of parts and products. As an alternative to 3D printing, laser cutting can be useful for flat components such as panels for a table, bookcase or shelving system and you are more likely to be able to make full size elements depending on the equipment you have in the workshop. Consider all of these as possible prototype outcomes but, whatever option you take, record the process and the feedback from testing and evaluation.
Notes: Feel free to edit / use these with your class as appropriate. Change the wording and share with students if you wish, or use to help your own planning.

## Slide 47: Test tasks
‘CAD testing’ | ‘Testing all parts’
Again, the use of modern CAD software brings a wealth of benefits including the ability to virtually ‘test’ your CAD models. As well as being able to test the visual aspects of your design through photorealistic rendering, animations and flythroughs, most software will have some aspect of FEA available. FEA allows you to specify the materials the furniture or components are made from, and the software calculates the mass, density, strength, elasticity etc. You can set fixed points where the model cannot move such as chair legs sitting on the floor or a handle attached to a drawer. You then specify the force being applied to parts of the model and how much load it being applied. The simulation will then run and show you where the strongest/weakest point would be and where they are likely to fail. You can then edit the model and rum the simulation again to see if you have made improvements. Repeat until you are happy with the results. Refer to the tutorials and instructions available with the software you are using or the supporting and curriculum units available with these contexts for further support. | You will need to test all aspects of the design, not just the finished product. Are all the individual parts made to a good standard, do they all fit together as intended? How easy or intuitive is it to assemble, operate or interact with? Are there any aspects that are not working as well as others? Sustainability is a key theme in this context and important to KI Europe. Also consider that in your testing. Could you reduce or minimise parts even more after testing without compromising aesthetics or performance? Remember that design is a process of continual improvement and there will always be room for improvement. You just have to decide how long you can spend improving a design. Remember also that testing the outcomes with users is an important aspect of User Centred Design. They should be involved throughout the process, but this is another chance to get valuable feedback on what may be your final proposal. As well as getting positive feedback, you can also watch the user interacting with your design and identify any problems they might have. Use this feedback to offer improvements and modifications for further iterations. Students should also refer back to their original defined statement or specification and discuss how well the prototype meets these criteria.
Notes: Feel free to edit / use these with your class as appropriate. Change the wording and share with students if you wish, or use to help your own planning.

## Slide 48: Level of challenge
Design contexts increase in challenge for each of the KS3 years. By reducing the scaffolding and support you can develop opportunities for more individual and innovative work to be produced.
Closed
Task
Open
Task
Context with Brief
Supported Context
Open Context
Simple foam or cardboard models that make use of existing components and concentrate more on form than function. These may be finished to look more like a commercial product even if they are not fully functional.
Greater focus on ergonomics and anthropometrics with the creation of functional CAD models that can be 3D printed or accommodate real components. Use of working components to test functionality.
A complete and working item of furniture can be fully tested. Ergonomics and anthropometrics considered as well as the use of 3D CAD and rapid prototyping or CNC technologies. Modular and adaptable designs considered.
Notes: Suggested levels of challenge. Use these for reference and set your own aims and objectives for the contexts.

## Slide 49: Competition opportunity
The Furniture Makers’ Company holds an annual competition / exhibition each year.
As part of this context, they welcome all participating schools to consider entering students’ designs / outcomes for this prestigious event.
Applications are open annually, opening from April to June, with an exhibition in the following October.
Notes: Please click the link in the text to find out more and how you can take part.