## Slide 1: Ki europe Supporting unit focused task: CAD modelling
Notes: Please note; This resource, accompanying resources and associated images, videos and graphics are to be used for educational purposes only and in line with our terms and conditions as stated here. https://www.designtechnology.org.uk/terms-and-conditions-and-policies/

## Slide 2: cad
Because design and innovation matter
Notes: This Focused Task provides an opportunity to learn some 3D CAD software which contextualising it to the KI Europe brief. You may wish to start more simply by creating a basic stool, or a simplified table may be more manageable. Later on, inspiration can be further drawn from rewatching the Ki videos and creating furniture solutions that minimise parts.

## Slide 3: cad
There are a wide range of CAD packages on the market and numerous tutorials for how to use and master the software.
You should choose the software that is best for your situation and needs based on the features it offers.
CAD can be used effectively to increase creativity, and to maximise your time and productivity. For this unit we will use Siemen’s Solid Edge which is a complete industry standard package free for students and teacher to use.
Please refer to the Technical Knowledge Curriculum Unit Solid Edge I for basic information about the software and interface etc.

## Slide 4: Creating a part
For this exercise, we will create a single-part chair much like the moulded plastic ones you might find in your garden. We can then use this for other applications such as rendering, drafting and FEA.
Start by choosing a Centre Rectangle from the Draw menu. If it’s not visible, click on the small arrow next to the rectangle to access a drop-down menu.
Notes: Using a centre rectangle is often preferable as it automatically gives you a centre datum point which can be really beneficial later on.

## Slide 5: Creating a part
You will now see the three planes that we can draw on. Choose the Top plane and click on the padlock icon to lock your drawing to this plane.

## Slide 6: Creating a part
Press CTRL and H to look directly at the Top plane to make drawing easier. Now click on the origin point and drag a rectangle. Let go of the mouse and type 400 then press the Tab button to move to the next and type 500. Press Enter twice to produce a rectangle (the first Enter confirms the angle of the rectangle).
You may have to zoom out to see the shape as its larger than the screen can show.

## Slide 7: Creating a part
Rotate the view so you can see the rectangle you just drew from an angle. Select the rectangle then click on the white arrow and drag up to form the shape. Type 60 (mm) for the height.
Select rectangle
Draw arrow upwards
Type 60 and Enter

## Slide 8: Creating a part
Let’s sculpt this shape to make a seat by drawing an arc on the side and then using it to delete part of the shape. Choose Arc by 3 Points and choose the long side of the shape. Draw a curve.
Click once to set the left of the arc, then the right and the final click in the middle lets you drag the curve of the arc.
Draw on the long side of the shape

## Slide 9: Creating a part
The arc has intersected the side of the shape allowing us to select the green area shown in the image. Use the arrow to ‘push’ this section into the shape and it will automatically remove it.

## Slide 10: Creating a part
Using the Corner Rectangle tool, draw a rectangle on the back are of the seat, around 70mm deep and the full width of the shape. Select that area and drag it up. Type 550 and Enter.
Draw rectangle
Select and drag upwards
Type 550 and Enter

## Slide 11: Creating a part
We can now start to define the shape of the seat using the Round tool. Apply a 60mm round to the top front and middle of the chair. Add some more to the edges to get a nice rounded shape.
Leave this edge square
60mm round here
Add some 50mm rounds to the edges

## Slide 12: Creating a part
Once you have the shape you are happy with, we can ‘shell’ the chair. In Solid Edge, this feature is known as Thin Wall. Select the two faces shown in green below and click on Thin Wall.
Choose these faces

## Slide 13: Creating a part
Type in 10mm for the wall thickness and press Enter. The part has now been made into a shell.
To add some support for the back and the legs, draw a rectangle around 80mm high and the width of the seat.

## Slide 14: Creating a part
Select the rectangle and use the arrow to drag it into the chair. Type 10 and press Enter and this new element should join with the existing chair shell.
Now, rotate the view to look under the chair.

## Slide 15: Creating a part
To make the next part easier, choose the bottom surface and press CTRL and H to look directly at it. Choose Corner Rectangle and select the same surface to lock on. Draw four squares in each corner, 70mm square.
Choose this face to look at and to draw the squares on.

## Slide 16: Creating a part
These square intersect the existing surface allowing you to select individual areas. Choose the front curve, click on the arrow and drag toward you to make a leg. Type 450 and Enter. Do the same for the other 3 corners of the chair base.
Draw arrow down
Type 450 and Enter
Select area

## Slide 17: Assigning materials
You now have a chair with four legs, and we are ready to assign materials. On the right-hand side of the screen is a toolbar. Select Style Palette and you will see a list of materials
Choose Polypropylene and drag the material onto the model. Experiment with different materials especially when we come to render.

## Slide 18: drafting
With a completed model, we can produce a draft. This is another term for a technical/working drawing. Go to the main menu and you will see Drawing of Active Model as an option. Choose this.
You have a few options but let’s try Creating standard views. Click OK.

## Slide 19: drafting
You can set first or third angle in your default settings and the views will automatically be assigned. Here we have a third angle projection as default, but we can select the views and rearrange them.
We can add more details, views, dimensions and more, but let’s look at the other option for creating a drawing first.

## Slide 20: drafting
If we run the View Creation Wizard, we will be given a blank drawing and can click to place a view. From this we can drag in different directions, and it will choose the relevant view. Click to place that view and carry on until you have all the views you need. This can include 3D isometric views as well as orthographic (flat views).

## Slide 21: drafting
With all your views in place, you can choose the style such as hidden line, solid etc. for each view. You can also add dimensions, make section and detailed views etc. These will be covered in more detail in another unit.

## Slide 22: Adjusting the model
We can make adjustments to the model without needing to make another draft. Here we can see an area of weakness in the frame, so let’s add some 80mm rounds to make it stronger.

## Slide 23: Adjusting the model
Let’s add some more details to the model such as adding cut outs in the back then rounding the corners off.

## Slide 24: Updating the draft
Because the draft is linked to our model, we simply have to choose Update Views, and the drawing is updated automatically to show the new features. Bear in mind that some dimensions may have changed, and we may need to add some more for the new features.

## Slide 25: rendering
Rendering is the process of generating a photorealistic or non-photorealistic image from a 2D or 3D model by the use of a computer program. Choosing CAD software that has the ability to render i.e. a built-in render engine, will allow you to quickly create these types of render from your models.

## Slide 26: rendering
Of the major/popular packages, Fusion, Solidworks, and Solid Edge have rendering engines built in. They can get impressive results with very simple settings and can show your models in a clean studio-like space or even place them into a real interior or exterior environment!

## Slide 27: rendering
In the Views tab, click on Keyshot Render. Because we have already assigned a material to the model, Keyshot places the object in a plain, studio-like, environment and calculates all the shadows and reflections without needing to do anything else. It already looks like a photograph, but we can still move the model around in real time.

## Slide 28: rendering
Clicking on an environment instantly puts your model into it complete with lights and reflections and, again, is ready to render out as a high-quality image with no need for complex settings.

## Slide 29: rendering
The same model in different materials and in a range of environments. Try experimenting with different settings to get the best effect.