## Slide 1: Ki europe Supporting unit focused task: 3d printing
Notes: Please note; This resource, accompanying resources and associated images, videos and graphics are to be used for educational purposes only and in line with our terms and conditions as stated here. https://www.designtechnology.org.uk/terms-and-conditions-and-policies/

## Slide 2: 3d printing
Because design and innovation matter

## Slide 3: 3d printing
3D Printing is becoming increasingly popular as a technique for making components and objects quickly and with relatively low expense. While the process started out using ABS or PLA, 3D printers can now work with food, metal and even organic materials such as human organs. It requires nothing other than printing material and a 3D model. It is a form of Rapid Prototyping Technology (RPT) which means you can quickly turn your ideas and designs into 3D prototypes. KI use it to help prototype their ideas for furniture.

## Slide 4: 3d printing
3D printing requires a 3D model which can be one that you made yourself or something downloaded from the internet.
Here we are using the chair created in Solid Edge in another supporting unit for this context.
Note that we modelled the chair to its true size which is likely to be much larger than most school 3D printers can produce.
We will look at scaling this model down when we come to 3D print it.

## Slide 5: Importing 3D objects
If you do not have files downloaded from the internet ready to 3D print, you will need a 3D model to export.
When importing 3D objects this way, they will not have any of the feature history from the software they created with. They will just be a mesh like the image on the right.
This is fine just to test out 3D printing, but you may struggle to make any edits to the model, and it may be that the geometry is not ‘clean’ which may cause some errors in 3D printing. Wherever possible, its best to make your own 3D models 

## Slide 6: Exporting the model
Depending on which software package you use, the process of exporting a 3D model will be slightly different. For example, in Tinkercad, there is an export button on the top right of the screen where you choose Export and then choose .STL format (a standard format for 3D printing). In Onshape you right click on the part tab and choose Export.
Because we are using Solid Edge there is a dedicated 3D print icon in the tool bar which, when opened offers you a simple Export button.

## Slide 7: Exporting the model
It is worth noting that Solid Edge defaults to inches when exporting for 3D printing, even if you have Millimetres set up as your units in the main options.
To get around this, choose Save As, then .STL as the type from the drop-down menu. Choose the Options tab and change Export Units to Millimetres.
Note that once you have done this manually, the 3D print option from the main menu will export in Millimetres by default.

## Slide 8: importing the model
We now need to open our 3D printing software which, for many printers, will be Cura (or often based on it). Open Cura and you will see a 3D model of the build plate. You can choose your printer from the setting menu if it is not already selected.

## Slide 9: importing the model
We can now go the main menu and choose Open File(s). It will then import the model, but you might be surprised by how big it is. Remember that the model was created full size!!
Build plate
3D model
Choose the .STL file you exported
Diagonal lines show the model is too big for the printer

## Slide 10: scaling the model
To the left of the screen are the navigation buttons. Select the 3D model and these become active. From here we can move, rotate, scale etc. Choose Scale and we can see the dimensions and that the scale is 100%.
Move
Scale
Rotate
Mirror

## Slide 11: scaling the model
Furniture models are often made 1:5 scale for visual purposes, so if we make the model 20% of the original size, we will have this scale. Note that the model still has diagonal lines on it. In this case, the height is just a little bigger than the 3D printer can accommodate.
Choose this to keep the model in proportion

## Slide 12: scaling the model
Let’s try making this a 1:10 model by choosing 10% scale in the settings.
The model is made smaller, and the diagonal lines disappear showing that this will fit on our 3D printer.

## Slide 13: printing the model
There are many options in Cura for fine tuning your 3D prints, and over time you will likely need to explore these.
However, you can get quick prints with Recommended settings, and you always have a preview of the print to check before starting to 3D print.
Print quality
Layer thickness
Infill
Supports
Build plate adhesion

## Slide 14: printing the model
With our settings made, we now simply press the Slice button and let the software work its magic. After a few seconds we see the output model, and also how long the print will take as well as how much filament is used.

## Slide 15: printing the model
We can switch to Preview mode to see how the print will look.
We can change the Colour scheme from Material Colour to Line Colour to better see what is being printed.

## Slide 16: printing the model
The build will take 3 hours 26 minutes and needs lots of supports, so let’s try rotating the object to see if this helps. Click on the red arc to rotate it so it is laying down.

## Slide 17: printing the model
Here we have also rotated it on the blue arc so it fits better on the build plate. Press Slice again and it has calculated that we will need less supporting material, use 10g less filament, and it will only take 2 hours 41 minutes.

## Slide 18: printing the model
We can try rotating it again, but this is introducing more supports (shown in blue) to the front of the chair. It will also take slightly longer to print.

## Slide 19: printing the model
We could try rotating it this way, but it takes as long as the original version (over 3 hours) and all of those supports we have to remove will leave marks on the parts of the chair that we want to look their best. This is not a good choice of orientation for a 3D print 

## Slide 20: printing the model
Let’s go back to the orientation that will take the least time and give use the best quality output (the top surfaces of a 3D print it usually the best quality).
Slice again. You can also see an animated preview of the print

## Slide 21: printing the model
We have a preview of the 3D print and, if we are happy with the settings, we need to save the file to disc (or send it to the printer if it is on a network).
Now we just need to load that file into the 3D printer and set it running. In a few hours you will have a real model to hold 