## Slide 1: Ki europe Supporting unit focused task: remote manufacture
Notes: Please note; This resource, accompanying resources and associated images, videos and graphics are to be used for educational purposes only and in line with our terms and conditions as stated here. https://www.designtechnology.org.uk/terms-and-conditions-and-policies/

## Slide 2: Remote manufacture
Because design and innovation matter
Notes: This Focused Task opens up lots of possibilities for classroom exploration. Part of the idea is to get students to value the importance of ensuring (where possible) their designs have been thoroughly checked before manufacture (whilst at the same time acknowledging rapid prototyping as a way to iterate). The stools could be 3D printed to test. You could allocate teams of students, a set amount of money and charge them for how long it takes, what material they use etc. Maybe even consider pairing with another school (or class) where some manufacture, some design…

## Slide 3: Remote manufacture
There are few companies that design products and also have the manufacturing capabilities to make those products. It is more common to have parts made remotely (away from the company’s base) and then either ship the products directly to the buyer, or have the parts send to a factory for assembly.
In this unit we will consider the brief to ‘minimise parts’ and create a simple stacking stool that can be made by moulding techniques.
We will look at the process of creating the stool in CAD and what would be necessary to have it manufactured remotely.

## Slide 4: Stacking stool brief
Modern manufacturing technology has made it affordable to rapidly prototype ideas without the needs for factories or workshops. Not everyone has access to these facilities, but the world of design is evolving, and many people now send their work off to be made by 3D print studios, maker boutiques etc. Situation: you are tasked with designing a space-saving seat that uses as few parts as possible, but you do not have the facilities necessary to make the product. Brief: design a small stacking stool that can be used in school for temporary seating. We will use this experience to explore how design works in the world of industry; where designers and makers are often miles or countries apart.

## Slide 5: CAD MODEL
Computer Aided Design (CAD) is now a standard tool in the designer’s arsenal, and most mass-produced products made today will be designed using some form of CAD.
For this tutorial we will be using Solid Edge, but you can use any parametric based CAD software. Please refer to the Curriculum Units for more detailed instructions for modelling, FEA, rendering etc.

## Slide 6: base
Because we need our stools to stack, we will need a draft (sloping) angle on our stool. The easiest way to do this will be to draw the shape we want, then remove unnecessary material. Start by drawing a square the size of the seat of the stool. 350x350mm should be fine. Extrude or sweep this by 400mm.

## Slide 7: base
Because we need our stools to stack, we will need a draft (sloping) angle on our stool. One way to do this is to choose a draft angle when extruding/sweeping the original rectangle. Solid Edge requires you to add the draft afterwards. Either way, choose 6 degrees as a draft angle.

## Slide 8: base
Let’s add 50mm rounds/fillets to each edge of the shape, but not the bottom face which we want to keep flat.

## Slide 9: base
Rotate your view so you are looking at the flat base and select it. Then choose the Thin Wall command to ‘shell the shape. We will try a thickness of 10mm for now then see how it performs when we test it later.

## Slide 10: base
We could use this as our final design, but we want to remove materials to leave four legs. Draw a shape using the line tool and dimension this to be 35mm from the edge of the rounded corners. You can change these dimensions to suit. Do this on two adjacent sides of the shape.

## Slide 11: base
Select one of the shapes you just drew and extrude it into the shape, but only enough to remove the 10mm wall. Don’t push it all the way through! Do the same on the adjacent side.

## Slide 12: base
Because it’s on a sloping side, the part we removed by extruding would not have cut through the other side the same way. We can choose the extrude/remove process from the feature tree and mirror it so it applies to the other side of the shape. Do the same on the adjacent side and you have your four- legged stool.

## Slide 13: base
We can add some rounds/fillets to the sharp corners to provide additional strength and to make the stool look more attractive.

## Slide 14: base
The final touch is to add some holes to the seat to reduce materials while also providing some ventilation. Draw a 25mm circle on the seat of the chair then extrude/remove it.

## Slide 15: base
We can use the Pattern tool to select the extruded process then choose rectangular pattern. We simply drag a rectangle from the centre of that hole and the software will automatically populate that rectangle with evenly spaced hoes!

## Slide 16: base
Here we can see the results of dragging that rectangular array on the seat of the stool. Finish off the model by adding some rounded corners to the holes you just made, and other hard and potentially sharp edges on the chair.

## Slide 17: Cad testing
Because we are not making the product, it’s important that we ‘test’ how it might perform under load. By using FEA, we can apply a load to the seat of the chair and see how it reacts. In this case, there is too much distortion meaning it will probably break. We could fix this by reinforcing the seat or making the shell thicker

## Slide 18: Generative design
Using the same material properties and criteria for where the force applied and fixed points, we can use generative design to change the form of the model to try and reduce weight/materials even further without reducing strength. What do you think of this design?

## Slide 19: Finished model
There is our finished stool. In assembly mode, we can simulate stacking the chairs and check that the draft angle allows for most of the stool to fit snugly into the one above it.

## Slide 20: rendering
Modern CAD software also has powerful built in rendering tools so we can see what the finished product would look like. We can also use this to show clients and manufacturers, what we expect the finished product to look like.

## Slide 21: Technical drawings
For the manufacturer to make the part exactly as it is designed, technical documents would need to be supplied, even if you were sending the 3D model to be used. This is to ensure the engineers can check all of the detail and make sure everything is approved before the expensive process of creating moulds.

## Slide 22: Technical drawings
Details of the stacking process which may be used for testing and how the products can be packaged to transport several at a time.

## Slide 23: Scales of production
Design and technology often involves making just one product each using a combination of hand tools and machinery. This is called a ‘one-off’. When you want to make more of the product you may move to ‘batch production’. To do this you would need to used jigs and templates so that each part can be the same. If you need to make very large numbers of the product you would move to mass production techniques which would mean investment in expensive CNC machinery, moulds etc. You would need to sell a lot of the product to recoup the cost of the initial investment.
For this stool, the design would not be practical for any process other than mass manufacture due to the use of moulding equipment.

## Slide 24: Scales of production
One-off
Batch
Mass production

## Slide 25: Injection moulding
Chairs like this are made through a process called injection moulding. While the cost to manufacture the moulds are relatively high, they can be used to produce items at very low cost so selling many of these would soon cover the initial costs of production and then become a very profitable item to manufacture.

## Slide 26: Bill of materials (BOM)
When making multi-component products, it is also important to produce a list of parts, sometimes known as a ‘Bill of Materials’. This lists all the parts needed, how many etc. so the manufacturer, or customers, can check that all the parts are present before assembling the product.
As we have designed a simple single part stool, the bill of materials is just one line, but it could include details such as material, weight etc.

## Slide 27: Just in time
In this image you can see how the product can be stacked to
save storage space and packaging. This has several benefits: Parts can be manufactured in large quantities and stored easily for transport Packaging can be stacked economically in storage should there be a great demand for the product (see JIT systems) Several item can be shipped in one box that is not much larger than need for a single item The product can easily be stored at home or in schools and colleges etc. saving space.

## Slide 28: Lean manufacture
Lean manufacture is a systematic approach to production which aims to eliminate all waste from product to production. To achieve this, we have taken several approaches to the design and manufacture of this product. The stool is moulded in one piece, so no material is wasted. The product stacks economically in use and for packaging for transportation, so it uses less packaging materials. There are no fittings or adhesives so no wasted materials or components. The product has been designed to use as little material as possible.
It can also be easily recycled as it is a single thermos plastic product.
The moulding process allows for high volume manufacture with little human input.

## Slide 29: remote manufacture
With all these factors considered, we have designed a product that meets the needs of the original context: to minimise parts. We have a single part stool suitable for mass manufacture by injection moulding. There are no additional components and no assembly. The items stack to save space in storage and transportation.
To have this made would involve sharing the 3D file and the technical drawings with the manufacturing company who would then provide the costs for tooling and production. All of this would happen away from the designer’s studio, or company premises which it why it is called ‘remote manufacture’.

## Slide 30: 3d printed model
To check the design of the stool, 3D printed models were created. Although much smaller than the intended full-size design, they can be used to check the look and proportion of the stool, and that they stack properly.