## Slide 1: Ki europe Supporting unit investigative & evaluative activity: finite element analysis (FEA)
Notes: Please note; This resource, accompanying resources and associated images, videos and graphics are to be used for educational purposes only and in line with our terms and conditions as stated here. https://www.designtechnology.org.uk/terms-and-conditions-and-policies/

## Slide 2: fea
Because design and innovation matter
Notes: Looking at virtual simulations may be a rather advanced step for some of your students, and show demonstrating that it is a feature, may be enough at an early stage. You may wish to explore an even more simplistic shape first, e.g. imagine a ruler being supported at one end and adding weight (like a springboard)

## Slide 3: Finite element analysis (FEA)
FEA in its simplest terms means virtual testing of products done in CAD by running a simulation of forces and stresses on a 3D model.
Many CAD packages now have simulation features built-in but do check if the CAD package you use has this feature. It is currently available in Fusion, Solidworks, and Solid Edge. Other packages may offer it as an ‘add on’.
For this unit, we will be using the simulation features in Solid Edge, but a similar process is followed by CAD software with this feature.

## Slide 4: What do I need?
To use FEA, you need a CAD package capable of running simulations and a 3D model to run the simulation on. Here we have created a very simple 3D model of a shell-style injection moulded chair.
We have deliberately kept the model quite thin and unsupported for this example, to exaggerate the effects of the simulation.

## Slide 5: Simulation
The key to working with this feature in Solid Edge is to work from left to right across the toolbar. So, after choosing New Study, we would Define parts of the model, apply the Force, then specify the Fixed elements.
We would then convert to a Mesh and finally press Solve to run the simulation.
There are many more detailed settings we could explore, but to perform a basic simulation on our design, this is all we need for now.
6. Solve
1. New Study
2. Define
4. Fixed
5. Mesh
3. Force

## Slide 6: Simulation
Before we can run a simulation, the software needs to know what materials we intend to make our product from. This is a single shell chair so we only need one material, and we will make this standard Polypropylene.
Note that the software already knows all the physical aspects of the material.
Choose the material and Apply to Model.

## Slide 7: define
With the simulation, you can apply different types of force on different elements in your model such as choosing castors or connecting pieces which will be behave differently in a chair. However, in this example, we have a single component plastic moulded chair so we can accept the default selected part.
The whole chair is highlighted as it is just one single component.

## Slide 8: force
Now we need to apply a force to the chair. Think about how a chair is intended to be used in its most basic form. The person would sit on it, and it would (hopefully) take their weight. So, choose Force and then select the seat of the chair. An arrow should appear.
Select this part of the chair
Steering wheel

## Slide 9: force
Move the blue sphere of the arrow to the centre of the seat and you will see the steering wheel. Hold Shift and click on the ring to rotate the arrow so it is pointing upwards. Note that the (blue) force arrows are pointing up. We need them pointing down so press ‘F’ to flip them.

## Slide 10: force
The last thing is to set the actual force being applied to the seat. The default value here is 1000 mN and an average young student might apply around 600 mN of force. Let’s leave the force at 1000 mN as this would show how the chair reacts under slightly heavier loads.
There will also be some force on the back of the chair, but we will add this later
Load on the seat and legs of the chair

## Slide 11: fixed
If we ran a simulation on this model now, the software would not know what points of the chair are fixed (imagine sitting on a chair while it is on ice). For our purposes, we think of the four legs as being fixed to the floor when someone sits on it. Choose Fixed and select the bottom faces of all four legs.
Select the face

## Slide 12: mesh
We now need to convert the model into a Mesh so the software can calculate how the material can flex and move more realistically. Choose Mesh from the menu and try the default settings for now.

## Slide 13: Mesh and solve
When we click on Mesh & Solve, the simulation runs and we see an image of the deformed chair. In this case pink is stable and stresses show from dark blue to green.
Choose the Animate option to see the deformation in real time.
Mesh & Solve

## Slide 14: Modify the force
A person is likely to lean back on the chair so let’s add another force to the back of the chair. Close the simulation and add a force as you did before, but this time 400 mN to the back of the chair.
As we already have the fixed elements and the previous force defined, we don’t need to go through it all again, just choose Solve to update the simulation.
Select this part of the chair

## Slide 15: Solve again
Now we can see the updated results. The force leaning back on the chair has reduced how much the chair seat bends, but the overall structure is still unstable and there are some very weak points where the seat meets the back which need to be addressed.
As well as areas of stress, there is a lot of movement in the legs

## Slide 16: Repair/improve
The great thing about this process, is that we can make changes to the 3D model and see how it improves the results of the simulation without setting it all up again. As long as we don’t remove the parts where we applied force or added fix points.
We can see that this area of the model is showing the greatest stress and is therefore the most likely to break!
What can we do to increase the strength of this area?

## Slide 17: Repair/improve
The frame has square corners and a thin seat which make it quite fragile. A simple edit is to add rounded corners to all the internal square corners on the chair.
Add rounded edges to all the internal corners of the chair

## Slide 18: Solve again
This updated model is much better, but there are still areas, shown in light green where the chair is likely to break under load.
Think about the plastic garden chairs you have sat on. Did they feel strong and stable? Have you ever broken one?
How could we further edit this chair at these weak points to reduce the chance of it breaking?

## Slide 19: Solved?
Compare the three versions. See how we have made the structure stronger and more stable each time. However, it would still need further improvement, as it is likely to break under load.

## Slide 20: Try this yourself
The simulation is virtual, but you could try applying these same forces to chairs in your home or school to see how they react. You could always base your model on an existing design and compare the results of the FEA and how the real object reacts.

## Slide 21: Classic chairs
FEA is a recent development, as is 3D CAD, but imagine how chairs from the past might have looked if the designers had access to this technology at the time. Try downloading free 3D models of some iconic chairs and running FEA on them to see how they react 